## Slide 1: Classical Networking Introduction
QuTech, Delft
© Bruno Rijsman, brunorijsman@gmail.com, 28 June 2019 v1

## Slide 2: The Internet: a network of networks
Notes: IP was originally intended to glue networks together using different protocols (X25, DECnet, IBM SNA). Now most all networks use IP also internally, with a few exceptions (SCADA industrial networks, Fibre channel in storage networks,

## Slide 3: Hosts: the end-point devices
User devices
Servers
IoT devices

## Slide 4: Tens of billions of end-point devices

## Slide 5: Hundreds of exabytes (1018 bytes) per month

## Slide 6: Autonomous systems: administrative domains
Service providers
Total > 50,000
Large companies
Notes: Operator or multi-homed enterprise. Can overlap topologically (”on top of each other” on map).

## Slide 7: Maps of the internet (at AS level of detail)

## Slide 8: Routers: devices that forward “IP” packets

## Slide 9: IPv4: unreliable datagram service
Packet by packet forwarding
Each packet has a destination IP address
Packets may be dropped, delayed, re-ordered, duplicated
End-points use higher-layer protocols (e.g. TCP) to make it reliable

## Slide 10: L3 Internet Protocol (IP): datagram service
IP
IP Header
IP
IP
IP
Laptop
L3 Router
L3 Router
Server

## Slide 11: L4 TCP: reliable end-to-end connections
IP
TCP
IP Header
TCP Header
IP
IP
IP
TCP
Laptop
L3 Router
L3 Router
Server

## Slide 12: L7 application protocol: e.g. HTTP, FTP, …
IP
TCP
HTTP
IP Header
TCP Header
IP
IP
IP
TCP
HTTP
Laptop
L3 Router
L3 Router
Server
HTTP Header
HTTP Payload

## Slide 13: L2 Ethernet: Local Area Network (LAN)
IP
Ethernet
TCP
HTTP
IP Header
TCP Header
Ethernet Header
Ethernet
IP
Ethernet
Ethernet
IP
Ethernet
IP
Ethernet
TCP
HTTP
Laptop
WIFI AP
L3 Router
L3 Router
L2 Switch
Server
HTTP Header
HTTP Payload

## Slide 14: L1 physical layers: WIFI, electrical, optical…
IP
Ethernet
Wifi
TCP
HTTP
IP Header
TCP Header
Ethernet Header
Ethernet
Optical
IP
Ethernet
Ethernet
Wifi
IP
Ethernet
Optical
Optical
IP
Ethernet
Optical
TCP
HTTP
Laptop
WIFI AP
L3 Router
L3 Router
L2 Switch
Server
ROADM
HTTP Header
HTTP Payload
Elec
Elec
Opt

## Slide 15: The OSI reference model
Layer number | Layer name | Responsibility | Examples
Layer 7 | Application | End-user functionality | HTTP, FTP, SMTP
Layer 6 | Presentation | Encoding | ASN.1, GPB, Thrift
Layer 5 | Session | Dialogue control, checkpointing | -
Layer 4 | Transport | Reliable end-to-end stream, end-to-end flow control, segmentation | TCP, QUIC, UDP
Layer 3 | Network | Global addressing, routing, fragmentation, quality of service. | IPv4, IPv6, IPX
Layer 2 | Datalink | MAC: Coordinate access to a shared medium. LLC: Group bits into frames, handle bit errors, point-to-point connections and flow-control | IEEE 802 series (Ethernet) PPP
Layer 1 | Physical | Send and receive bits over physical medium. | Ethernet 1000BASE-T SONET/SDH

## Slide 16: Each end-point has an IP address (IPv4 or IPv6)
140.13.8.12
140.13.243.22
140.13.12.99
140.13.106.3
45.9.3.17
45.9.3.28
45.9.3.102
45.9.3.87
13.224.5.2
13.224.13.9
13.225.7.9
13.231.8.19
13.243.77.102
Notes: Routers also known as gateways (for example Border Gateway Protocol) for historical reasons.

## Slide 17: IP addresses have topological significance
140.13.8.12
140.13.243.22
140.13.12.99
140.13.106.3
45.9.3.17
45.9.3.28
45.9.3.102
45.9.3.87
13.224.5.2
13.224.13.9
13.225.7.9
13.231.8.19
13.243.77.102
13.224.0.0 / 12
45.9.3.0 / 24
140.13.0.0 / 16
IP addresses can be aggregated (= summarized) into IP prefixes

## Slide 18: Routers do lookup in forwarding table (FIB)
Host
H1
Router
R1
10.1.1.2
Host
H4
1
10.3.2.2
Host
H2
10.2.1.2
Router
R2
Host
H3
10.3.1.2
2
3
1
2
3
Destination | Next-hop
10.1.1.2 / 32 | Interface 1
10.2.1.2 / 32 | Interface 2
10.3.1.2 / 32 | Interface 3
10.3.2.2 / 32 | Interface 3
Forwarding table (FIB) of router R1
Looks up the destination IP address for each individual packet
Destination | Next-hop
10.1.1.2 / 32 | Interface 1
10.2.1.2 / 32 | Interface 1
10.3.1.2 / 32 | Interface 2
10.3.2.2 / 32 | Interface 3
Forwarding table (FIB) of router R2

## Slide 19: Aggregation and longest prefix match
Host
H1
Router
R1
10.1.1.2
Host
H4
1
10.3.2.2
Host
H2
10.2.1.2
Router
R2
Host
H3
10.3.1.2
2
3
1
2
3
Destination | Next-hop
10.1.1.2 / 32 | Interface 1
10.2.1.2 / 32 | Interface 2
10.3.0.0 / 16 | Interface 3
Forwarding table (FIB) of router R1
Use aggregation to reduce forwarding table size
Default route is special case
10.3.0.0/16
Destination | Next-hop
0.0.0.0 / 0 | Interface 1
10.3.1.2 / 32 | Interface 2
10.3.2.2 / 32 | Interface 3
Forwarding table (FIB) of router R2

## Slide 20: Addressing
Datalink: Ethernet address
  Just happens to be globally unique
  No topological significance (“flat address space”)
  Not managed (burned into chip)
Network: IPv4 address (32 bits) or IPv6 address (128 bits)
  Originally intended to be unique on the Internet
  Private IP addresses (e.g.10/8), NAT, and anycast complicate matters
  Topological significance; allows for aggregation; makes the Internet scale
  Very carefully managed (complex procedures for allocating and assigning IP addresses)
Transport: Port numbers
  Identify service (“socket”) running on a particular server
Notes: Routers also known as gateways (for example Border Gateway Protocol) for historical reasons.

## Slide 21: Naming
Domain name: human readable name
Identifies a service
Example: www.google.com (not https://www.google.com/somepage)
The Domain Name System (DNS) protocol translates a name to an IP address
One DNS name can map to multiple different IP addresses (for load balancing – other mechanisms exist as well)
The mappings can change over time (for resilience)
DNS is highly decentralized and scalable
Notes: Routers also known as gateways (for example Border Gateway Protocol) for historical reasons.

## Slide 22: Control plane versus data plane
Router
Control Plane
(software)
Data Plane
(usually hardware)
Control plane
Discover network topology and resources
Program the forwarding plane (e.g. forwarding table)
Flexibility is main concern
Data plane (aka forwarding plane)
Forward packets
Using the forwarding table populated by the control plane
Speed is main concern

## Slide 23: Control plane versus data plane
Router
Control Plane
(software)
Data Plane
(usually hardware)

## Slide 24: Control plane - data plane interface
Router
Control Plane
(software)
Data Plane
(usually hardware)
Control plane – data plane interface
Configure networking devices (e.g. set interface address)
Program forwarding plane (e.g. add entry to forwarding table)
Send and receive control plane packets (”punting”)
Retrieve statistics
Historically proprietary (SDK provided by chip vendor)
Standards: ForCES, OpenFlow, SAI, Netlink, P4 generated…

## Slide 25: “Traditional” distributed control plane
Router
Control Plane
Data Plane
Router
Control Plane
Data Plane
Router
Control Plane
Data Plane
Control plane protocols OSPF, ISIS, BGP, PIM, RSVP, LDP, …
Data plane protocols IPv4, IPv6, MPLS, …
API proprietary, ForCES, OpenFlow, SAI, P4 generated…
Notes: Out-of-band vs in-band.

## Slide 26: SDN: centralized control plane (simplified)
Forwarding element
Data Plane
Forwarding element
Data Plane
Forwarding element
Data Plane
Controller
Control Plane
Data plane protocols IPv4, IPv6, MPLS, …
API proprietary, ForCES, OpenFlow, SAI, P4 generated…
Notes: Out-of-band vs in-band.

## Slide 27: Example forwarding plane chip
Broadcom Tomahawk 3
12.8 terrabits per second (Tbps)
128 x 100G interfaces
8 billion packets per second
0.04 nano seconds to forward 1 packet
Relatively small forwarding tables (480K)
Shallow buffers (internal shared 64MB)
Lean feature set

## Slide 28: The responsibilities of the forwarding plane
For each packet: layer 3 longest prefix match lookup of destination IP address
Actually, a lot more than that:
Layer 2 exact match lookup of destination Ethernet address
Buffer packets in case of congestions
Scheduling for Quality of Service (QoS)
Lookup of source address for validation and learning
Compute hash for Equal Cost Multipath (ECMP)
Apply policies (ACLs)
Track metrics (counters, thresholds, …)
Make copies for multicast and taps
… etc. etc. etc.

## Slide 29: Example fixed forwarding spipeline

## Slide 30: Traditional distributed routing protocols
Intra-domain routing protocols
  Exchange routes inside autonomous system
  All routers owned and operated by same organization
  Higher level of trust, more information available
  Emphasis on shortest path
  Example: OSPF, ISIS, EIGRP, RIP, RIFT, BGP (!), ….
Inter-domain routing protocols:
  Exchange routes between autonomous systems
  Routers owners by different organizations
  Lower level of trust, less information available, real money is involved
  Emphasis on implementing business policies (customers, transit, peering, …)
  Only one protocol: BGP version 4

## Slide 31: Routing protocol algorithms
Link State Routing
  Every router discovers full topology and computes shortest path
  The dominant algorithm for intra–domain routing
  Open Shortest Path First (OSPF)
  Intermediate-System to Intermediate-System (ISIS)
Vector Routing
  Distance-Vector or Path-Vector
  Routers do not know full topology
  Each router locally choses best path and propagates that path
  Routing Information Protocol (RIP)
  Border Gateway Protocol (BGP)

## Slide 32: Intra-domain vs inter-domain (simplified)
OSPF
ISIS
ISIS
BGP
BGP
BGP
BGP

## Slide 33: Other control plane protocols
Traffic engineering protocols:
  Used to
  RSVP, LDP, BGP-LU, ISIS-TE, OSPF-TE, Segment Routing
Multicast protocols:
  IGMP, MLD, PIM (several modes)
Service protocols:
  L3VPN, L2VPN, EVPN, …
Management protocols:
  SSH, SNMP, NETCONF, FTP, …
Telemetry protocols
  NetFlow, GPB, …
Notes: Routing

## Slide 34: Next seminars
Deeper dive into routing protocols
  Open Shortest Path First (OSPF)
  Intermediate System to Intermediate System (ISIS)
  Border Gateway Protocol (BGP)
Traffic engineering
  Multi-Protocol Label Switching (MPLS)
  Resource Reservation Protocol (RSVP)
  Path Computation Element Protocol (PCEP)
Software Defined Networking (SDN)
  SDN motivations and applications
  OpenFlow
  Programming Protocol-independent Packet Processors (P4)
Notes: Routing