## Slide 1: Routing in the Classical Internet
QuTech, Delft
© Bruno Rijsman, brunorijsman@gmail.com, 3 July 2019 v1

## Slide 2: Intra-domain vs inter-domain routing
Intra-domain routing protocols (IGP = Interior Gateway Protocol)
  Exchange routes inside autonomous system
  All routers owned and operated by same organization
  Higher level of trust, more information available
  Emphasis on shortest path
  Example: OSPF, ISIS, EIGRP, RIP, RIFT, BGP (!), ….
Inter-domain routing protocols (EGP = Exterior Gateway Protocol)
  Exchange routes between autonomous systems
  Routers owners by different organizations
  Lower level of trust, less information available, real money is involved
  Emphasis on implementing business policies (customers, transit, peering, …)
  Only one protocol: BGP version 4

## Slide 3: Intra-domain vs inter-domain routing
OSPF
ISIS
ISIS
BGP
BGP
BGP
BGP

## Slide 4: Routing protocol algorithms
Link State Routing
  Every router discovers full topology and computes shortest path
  The dominant algorithm for intra–domain routing
  Open Shortest Path First (OSPF)
  Intermediate-System to Intermediate-System (ISIS)
Vector Routing
  Distance-Vector or Path-Vector
  Routers do not know full topology
  Each router locally choses best path and propagates that path
  Routing Information Protocol (RIP)
  Border Gateway Protocol (BGP)

## Slide 5: Unicast vs multicast routing
Unicast routing protocols
  Each packet is delivered to single destination
  Destination IP address is unicast IP address (could be anycast)
  Most traffic on the internet (including video-on-demand)
  Most routing protocols: OSPF, ISIS, BGP, …
Multicast routing protocols
  Each packet is delivered to a group of zero or more destinations (“listeners”)
  Destination IP address is multicast IP address (224.x.x.x – 239.x.x.x)
  Example application: live broadcast TV
  Signaling protocols for listeners to join and leave a group: IGMP, MLD
  Routing protocols to create distribution tree in the network: PIM
  Not relevant for Quantum networks (no-cloning)? Or maybe multi-partite entanglement?

## Slide 6: Deep dive into BGP
What makes BGP so interesting?
It is the one and only routing protocol that is used across the entire Internet; to understand the Internet you must understand BGP.
It is not just about finding the shortest path; it has a very rich “policy” framework to reflect business requirements.
The scaling challenges are enormous; store 1+ million routes in the route table; advertise 1+ billion routes in a few minutes; …
The feature richness is bewildering:
  Many services beyond IPv4/IPv6 Internet: L3VPN, VPLS, EVPN, LS-BGP, …
  Cannot upgrade the Internet all at once: capabilities, etc.
  There is no scheduled downtime for the Internet: NSF, NSR, …

## Slide 7: Example Internet topology
Content provider
Enterprise
Dual-homed
Enterprise
Single-homed
Consumer
Consumer
Consumer
Notes: Transit service. Settlement-free peering. Valley-free routing.

## Slide 8: Commercial relationships in the Internet
Peers
Tier-1 Service Providers
Content provider
Enterprise
Dual-homed
Consumer
Enterprise
Single-homed
Consumer
Consumer
Provider
Customer
$$$
$
Provider
Customer
$$
Provider
Customer
$
Peers
$
Notes: Transit service. Settlement-free peering. Valley-free routing.

## Slide 9: Internet eXchange Point (IXP)
L3
L3
L3
L3
L3
L2
BGP route server
IXP
Layer 2 switch
Bilateral peering
Internet Exchange Point

## Slide 10: Provider – customer traffic
$
$
$
$
Content provider
Transit service
$
$
Consumer
Enterprise
Dual-homed
Enterprise
Single-homed
$
$
$
$
$
$
Consumer
Consumer
Consumer
Transit service
Notes: Transit service. Settlement-free peering. Valley-free routing.

## Slide 11: Peer – peer traffic
$
$
$
$
Content provider
$
$
Consumer
Enterprise
Dual-homed
Enterprise
Single-homed
$
$
$
Consumer
Consumer
Consumer
$
$
Settlement-free peering
$
Notes: Transit service. Settlement-free peering. Valley-free routing.

## Slide 12: Valley-free routing
Content provider
Consumer
Enterprise
Dual-homed
Enterprise
Single-homed
Consumer
Consumer
Consumer
Providers must not transit traffic through their customers
Notes: Transit service. Settlement-free peering. Valley-free routing.

## Slide 13: Peering is for direct customer traffic only
Content provider
Consumer
Enterprise
Dual-homed
Enterprise
Single-homed
Consumer
Consumer
Consumer
Don’t abuse peering to make someone else pay for transit
$
$
$
Notes: Transit service. Settlement-free peering. Valley-free routing.

## Slide 14: BGP neighbors and BGP sessions
Autonomous
System
Autonomous
System
BGP neighbor
BGP neighbor
BGP session

## Slide 15: IBGP versus EBGP
EBGP = External BGP = Between different AS
Normally between directly connected EBGP neighbors
IBGP = Internal BGP= Inside one AS
Often, IBGP neighbors are not directly connected (multi-hop BGP session)
EBGP
EBGP
IBGP

## Slide 16: IBGP full mesh
EBGP
EBGP
EBGP
Full mesh of N2 IBGP multi-hop IBGP sessions
Because no IBGP to IBGP route propagation, because AS-Path not used for IBGP loop detection
IBGP
IBGP session between A and B
but no physical link between A and B!
B
A

## Slide 17: Ways to reduce IBGP full mesh
Route reflector
BGP-free core
Tunnel mesh (LSP or GRE)
Confederation
“Nested” AS
Route reflector
Tunnel
sub-AS

## Slide 18: BGP sessions run over TCP
BGP relies on TCP for reliability and flow-control
BGP is not a periodic protocol (advertise once, withdraw explicitly)
TCP cannot detect failure in the absence of traffic (hence KEEPALIVE)
Chicken-and-egg problem? No, TCP uses IGP routes to connect.

## Slide 19: OPEN: Establishing a BGP session
OPEN message is sent to initialize BGP session
First message after TCP connection established
Both sides initiate TCP connection; rules for collisions
Fields:
  Version: 4
  Local AS number
  BGP identifier: router ID
  Proposed hold time: time-out for KEEPALIVE
  Capabilities: negotiate optional features (multiprotocol, route refresh, 4-octet AS numbers, many more…)

## Slide 20: NOTIFICATION: Closing a BGP session
NOTIFICATION message is sent to terminate BGP session
Scheduled (”Cease”) or error condition
TCP connection is closed
All routes from BGP neighbor are removed when BGP session goes down for any reason (exception: graceful restart).
This is a “heavy hammer”
Fields:
  Error code: general category of problem
  Error subcode: more detailed cause of error
  Error data: more details about the error

## Slide 21: KEEPALIVE: Check liveness
KEEPALIVE is sent periodically to check liveness of TCP connection in absence of other traffic
Sent 1/3 of negotiated hold-time (typically every 30 seconds, but often configured to be sent much faster)
If not received 3x in a row, hold time expired NOTIFICATION is sent.

## Slide 22: UPDATE: Advertise routes
A
B
EBGP
1.1.0.0/16
2.2.2.0/24
UPDATE
UPDATE
Advertise 1.1.0.0/16
Advertise 2.2.2.0/24
2.2.2.0/24 → B
1.1.0.0/16 → A
Route table
Route table

## Slide 23: UPDATE propagation over multiple ASs
1.1.0.0/16
A
B
EBGP
C
D
EBGP
E
F
EBGP
IBGP
IBGP
UPDATE
1.1.0.0/16
Nexthop A
UPDATE
UPDATE
UPDATE
UPDATE
1.1.0.0/16
Nexthop B
1.1.0.0/16
Nexthop C
1.1.0.0/16
Nexthop D
1.1.0.0/16
Nexthop E
Note: for the sake of simplicity example assumes single-hop IBGP sessions and next-hop-self on IBGP sessions
1.1.0.0/16 → A
1.1.0.0/16 → C
1.1.0.0/16 → E
1.1.0.0/16 → B
1.1.0.0/16 → D

## Slide 24: Indirect nexthop resolution
B
D
C
A
UPDATE
1.1.0.0/16
Nexthop A
UPDATE
1.1.0.0/16
Nexthop B
EBGP
IBGP
OSPF
OSPF
IBGP
UPDATE
1.1.0.0/16
Nexthop B
IBGP
OSPF B → C
BGP 1.1.0.0/16 → C
BGP 1.1.0.0/16 → B
BGP indirect nexthop B
Resolved to direct nexthop C
using OSPF route

## Slide 25: AS path for loop detection
IBGP
EBGP
EBGP
EBGP
A
B
C
D
AS 100
1.1.0.0/16
AS 200
AS 300
UPDATE
1.1.0.0/16
AS path 300 200 100
UPDATE
1.1.0.0/16
AS path 100
UPDATE
1.1.0.0/16
AS path 200 100
Router A ignores this UPDATE because of
AS Path loop
1.1.0.0/16
AS path 200 100
UPDATE

## Slide 26: AS path for shortest path selection
AS 100
1.1.0.0/16
AS 200
AS 300
AS 400
AS 500
1.1.0.0/16
AS path 100
1.1.0.0/16
AS path 100
1.1.0.0/16
AS path 200 100
1.1.0.0/16
AS path 400 300 100
1.1.0.0/16
AS path 100
1.1.0.0/16
AS path 300 100
1.1.0.0/16
AS path 300 100
D
1.1.0.0/16
AS path 200 100
1.1.0.0/16
AS path 100
Router C has two routes to prefix 1.1.0.0/16:
One received from A with AS path 200 100
One received from B with AS path 400 300 100
C selects the route from A with the shortest AS path as the best route
The best route is installed in the forwarding table
The best route is propagated to router D
C
B
A

## Slide 27: Information in a BGP UPDATE
Withdrawn prefixes (NLRI)
Advertised prefixes (NLRI)
Attributes of advertised prefixes
  Origin
  AS Path: loop detection and shortest path selection
  Nexthop: indirect nexthop, which is resolved to direct nexthop using IGP
  Multi-Exit Discriminator (MED): indicate preferred entry-point into my AS
  Local preference: indicated preferred exit-point from my AS
  Atomic aggregate
  Aggregator: who created an aggregate route (summary route)
  Optional extensions to BGP added ~30 more attributes, e.g. cluster-list https://www.iana.org/assignments/bgp-parameters/bgp-parameters.xhtml#bgp-parameters-2

## Slide 28: Network Layer Reachability Information (NLRI)
Originally IPv4 prefix
Later generalized to other address families, e.g. IPv6
Later generalized to key of table being synchronized
  Layer 3 Virtual Private Networks (L3 VPN)
  Ethernet Virtual Private Network (EVPN)
  Etc.
BGP has almost turned into an eventually consistent general-purpose database synchronization protocol (controversial)

## Slide 29: The decision process (= path selection)
Nexthop must be reachable
Lowest weight
Highest local preference
Prefer locally generated
Shortest AS path length
Origin: prefer
Lowest MED
Prefer EBGP over IBGP
Lowest metric of IGP route that resolves indirect nexthop
Declare ECMP if multipath is enabled
For external paths, prefer first received
Lowest router ID
Lowest cluster list
Lowest neighbor address

## Slide 30: Example BGP route (Juniper)
user@R4> show route 100.100.1.0 detail
inet.0: 20 destinations, 24 routes (20 active, 0 holddown, 0 hidden)
100.100.1.0/24 (2 entries, 1 announced)
*BGP Preference: 170/-201
Source: 10.0.0.2
Next hop: 10.1.24.1 via so-0/0/3.0, selected
Protocol next hop: 10.0.0.2 Indirect next hop: 8644000 277
State: <Active Int Ext>
Local AS: 65002 Peer AS: 65002
Age: 2:22:34 Metric: 5 Metric2: 10
Task: BGP_65002.10.0.0.2+179
Announcement bits (3): 0-KRT 3-BGP.0.0.0.0+179 4-Resolve inet.0
AS path: 65001 I
Localpref: 200
Router ID: 10.0.0.2
BGP Preference: 170/-101
Source: 10.1.45.2
[...]

## Slide 31: BGP policies
Policy is the central concept in BGP
  It allows BGP to implement reflect business rules (money is involved)
  BGP policy is much richer than policy in any other routing protocol
Policy rules describe:
  Which routes should be accepted from a BGP neighbor
  Which routes should be advertised to a BGP neighbor
  How the attributes of accepted and advertised routes should be modified
It explains why BGP is a “path vector” protocol
Each router vendor has its own policy language

## Slide 32: RIB-In, RIB-Local, RIB-Out, FIB
RIB-Out
RIB-Out
RIB-In
A
B
C
Routes from A before inbound policy
Routes from A after inbound policy
Routes to A after outbound policy
Best Routes
before outbound policy
Routes from B before inbound policy
Routes from B after inbound policy
Routes to B after outbound policy
Routes from C before inbound policy
Routes from C after inbound policy
Routes to C after outbound policy
FIB
Best routes
across all protocols
Inbound policy
Best path selection

## Slide 33: Example policy (Cisco)
router bgp 130
network 121.10.0.0 mask 255.255.224.0
neighbor 120.1.5.1 remote-as 120
neighbor 120.1.5.1 prefix-list aggregate out
neighbor 120.1.5.1 route-map routerD-out out
neighbor 120.1.5.1 prefix-list default in
neighbor 120.1.5.1 route-map routerD-in in
!
ip prefix-list aggregate permit 121.10.0.0/19
ip prefix-list default permit 0.0.0.0/0
!
route-map routerD-out permit 10
set as-path prepend 130 130 130
!
route-map routerD-in permit 10
set local-preference 80

## Slide 34: Example: Internet Service Provider (ISP)
Tier-1
Provider
AS 200
ISP
AS 300
2.2.2.0/24
Tier-1
Provider
AS 100
ISP AS 400
Customers 1.1.0.0/16
ISP AS 500
3.3.0.0/16
Customers only (prepend) 1.1.0.0/16 400 400 400
Full Internet
2.2.2.0/24 100 300
3.3.0.0/16 100 200 500
+ 800,000 more routes
Customers only 1.1.0.0/16 400
Full Internet
2.2.2.0/24 200 100 300
3.3.0.0/16 200 500
+ 800,000 more routes
Full Internet

## Slide 35: Single-homed enterprises
ISP
AS 300
Enterprise 1.1.14.0/24
Enterprise 1.1.27.0/24
Tier-1
Provider
AS 100
ISP
AS 400
Enterprise 2.17.13.0/24
Enterprise 2.17.98.0/24
Tier-1
Provider
AS 200
Customer route 1.1.14.0/24 65000
Customer route 1.1.27.0/24 65001
Default only
0.0.0.0/0 400
Default only
0.0.0.0/0 400
Full Internet
1.1.0.0/16 300
+ 800,000 more routes
Full Internet
1.1.0.0/16 200 100 300
+ 800,000 more routes
Full Internet
1.1.0.0/16 100 300
+ 800,000 more routes
Advertised routes
Inbound traffic
Received routes
Sent traffic

## Slide 36: Dual-homed enterprise (active-standby)
ISP
AS 100
ISP
AS 200
Enterprise AS 300
Customer route
7.7.7.0/24 300
The rest
of the Internet
Inbound traffic
Active Link
Standby
Customer route
7.7.7.0/24 300 300 300 300 300
Full Internet
7.7.7.0/24 100 300
+ 800,000 more routes
Full Internet
7.7.7.0/24 200 300 300 300 300 300
+ 800,000 more routes

## Slide 37: Dual-homed enterprise (active-standby)
ISP
AS 100
ISP
AS 200
Enterprise AS 300
Default route only
0.0.0.0/0 100
The rest
of the Internet
Outbound traffic
Active Link
Standby
Default route only
0.0.0.0/0 200
Full Internet
+ 800,000 routes (incl 7.7.7.0/24)
Full Internet
+ 800,000 routes (incl 7.7.7.0/24)
Inbound policy:
Set local-pref 200
Imbound policy:
Set local-pref 150
Default route only
0.0.0.0/0 100 Local-pref 200
Default route only
0.0.0.0/0 100 Local-pref 150

## Slide 38: Dual-homed enterprise (a-s optimized)
ISP
AS 100
1.1.1.0/24
ISP
AS 200
2.2.0.0/16
Enterprise AS 300
Default + customers
0.0.0.0/0 100
1.1.1.0/24 100
The rest
of the Internet
Outbound traffic
Active Link
Standby
Default + customers
0.0.0.0/0 200
2.2.0.0/16 200
Full Internet
+ 800,000 routes (incl 7.7.7.0/24)
Full Internet
+ 800,000 routes (incl 7.7.7.0/24)
Inbound policy:
Set local-pref 200
Imbound policy:
Set local-pref 150
Default route only
0.0.0.0/0 100 Local-pref 200
1.1.1.0/24 100 Local-pref 200
Default route only
0.0.0.0/0 200 Local-pref 150
2.2.0.0/16 200 Local-pref 150

## Slide 39: BGP security is severely lacking
Resource Public Key Infrastructure (RPKI) proposed to fix some of the problems.
BGP trust model makes

## Slide 40: Advanced BGP topics (We just scratched the surface)
BFD
BGP in datacenters
BGP over GRE
BGP over MPLS
Capability negotiation
Communities
Confederations
Extended communities
EVPN
Flowspec
Inter-AS VPNs a b c
L2VPN
L3VPN
Labeled Unicast
Link State BGP
Link State BGP
Multihoming
Multipath
Outbound Route Filters
Redistribution
Route reflectors
Route servers
RPKI
SD-WAB
Secure BGP
Segment Routing
YANG models
Etc. etc. etc….