## Slide 1: Traffic Engineering (TE)
QuTech, Delft
© Bruno Rijsman, brunorijsman@gmail.com, 11July 2019 v1

## Slide 2: Stateless hop-by-hop IP forwarding
Router
R1
Router
R2
Router
R3
28.7.23.3
Destination | Next-hop
… | …
28.7.23.0/24 | Router R3
… | …
Destination Address
IP Packet
Router
R4
Forwarding Table

## Slide 3: Example network
Router
R1
Router
R3
Router
R5
Router
R4
Router
R2
Router
R6
Router
R7
Router
R8
Router
R9
10 Gbps
10 Gbps
10 Gbps
10 Gbps
10 Gbps
10 Gbps
10 Gbps
10 Gbps
10 Gbps

## Slide 4: Congestion due to shortest-path forwarding
Router
R1
Router
R3
Router
R5
Router
R4
Router
R2
Router
R6
Router
R7
Router
R8
Router
R9
8 Gbps
8 Gbps
Congestion
Congestion

## Slide 5: Traffic engineering to avoid congestion
Router
R1
Router
R3
Router
R5
Router
R4
Router
R2
Router
R6
Router
R7
Router
R8
Router
R9
8 Gbps
8 Gbps
Non-shortest path

## Slide 6: When is TE used in classical networks?
TE only matters if there is (potential) congestion
Traffic demand is high relative to available bandwidth
Traffic demand does not automatically adapt (e.g. TCP back-off)
Application is sensitive to latency, jitter, or drops (e.g. video or voice)
Over-provisioning the network is not an option
Cost of recovery in application layer is high (e.g. Wide Area Network)
TE only works if traffic demand is known / predictable
Traffic demand can be measured
Traffic demand follows predictable pattern (e.g. diurnal pattern)
Or, traffic demand can be scheduled (e.g. Google internal backbone)

## Slide 7: Lessons for quantum networks
Bandwidth on quantum networks is extremely scarce
  10s to 100s of Bell pairs per second on point-to-point links
  End-to-end Bell pairs may be even less (probabilistic swap, distillation, …)
”Congestion” is not acceptable
  Stored qubits have short decoherence times
  Queueing delays will cause decoherence and loss of fidelity
Traffic engineering makes sense for quantum networks

## Slide 8: Traffic engineering functional blocks
Path
Computation
Signal paths
Install paths into forwarding plane
Discover topology and available resources
Network topology
Available resources
Traffic demand
Other constraints
Optimal routes for paths
Discover traffic demand and other constraints

## Slide 9: Classical traffic engineering protocols
CSPF
Distributed Constrained Shortest Path First
or
PCE
Centralized Path Computation Element
RSVP / Segment routing
Resource reservation protocol
(G)MPLS
(Generalized) Multi-Protocol Label Switching
ISIS-TE / OSPF-TE
Intermediate System to Intermediate System or Open Shortest Path First with Traffic Engineering Extensions
Network topology
Available resources
Traffic demand
Other constraints
Optimal routes for paths
NetFlow / IPFIX
Manual configuration

## Slide 10: Topology discovery
RSVP / Segment routing
Resource reservation protocol
ISIS-TE / OSPF-TE
Intermediate System to Intermediate System or Open Shortest Path First with Traffic Engineering Extensions
Network topology
Available resources
Traffic demand
Other constraints
Optimal routes for paths
NetFlow / IPFIX
Manual configuration
CSPF
Distributed Constrained Shortest Path First
or
PCE
Centralized Path Computation Element
(G)MPLS
(Generalized) Multi-Protocol Label Switching

## Slide 11: Discover topology using link-state routing
There are two widely used link-state routing protocols:
Open Shortest Path First (OSPF)
Intermediate System to Intermediate System (ISIS)
They are very similar. Each router:
Discovers direct neighbors (“adjacencies”) using hello packets
Summarizes all adjacencies in a link-state packet
Reliably floods its own link-state packet to all other routers
Stores the link-state packets from all other routers in a database
Constructs the topology of the network from the link-state database

## Slide 12: Link state packet reports adjacencies
Link-state packet originated by R5
R1
R2
R3
R4
R5
R6
R7
R8
R9
Adjacency | Metric
R3 | 10
R4 | 10
R8 | 10
R3
R4
R5
R8

## Slide 13: Initial flooding of link-state packets (LSPs)
R1
R2
R3
R4
R5
R6
R7
R8
R9
LSP is identified by originator + type + identifier + version number
Originator initiates flooding whenever LSP changes (e.g. adjacency up or down)
Originator sends LSP to all adjacencies
Receiver checks: do I have LSP version in database?
If yes, ignore.
If no:
  Store LSP in database
  Flood LSP to all adjacencies, except the one it was received from

## Slide 14: Making the flooding reliable: acknowledgements
R1
R2
LSA Header |  |  |  | LSA Content
Type | ID | Advertising router | Sequence number | 
… | … | … | … | …
Router-LSA | 1.1.1.1 | Router R1 | 20 | …
Router-LSA | 9.9.9.9 | Router R9 | 14 | …
… | … | … | … | …
Link state database (LSDB) of R1
Link-State Update
LSA = Router : 1.1.1.1: R1 : 20 + content
Link-State Acknowledgement
LSA header = Router : 1.1.1.1: R1 : 20
Link-State Update
LSA = Router : 9.9.9.9: R9 : 14 + content
Link-State Acknowledgement
LSA = Router : 9.9.9.9: R9 : 14
Link-State Update
LSA = Router : 9.9.9.9: R9 : 14 + content
Time-out

## Slide 15: Initial sync: database description + request
R1
R2
LSA Header |  |  |  | LSA Content
Type | ID | Advertising router | Sequence number | 
… | … | … | … | …
Router-LSA | 1.1.1.1 | Router R1 | 20 | …
Router-LSA | 9.9.9.9 | Router R9 | 14 | …
… | … | … | … | …
Link state database (LSDB) of R1
Database Description
LSA-header = Router : 1.1.1.1: R1 : 20
LSA-header = Router : 9.9.9.9 : R9 : 14
Link-State Request
LSA-header = Router : 1.1.1.1: R1 : 20
LSA-header = Router : 9.9.9.9 : R9 : 14
Link-State Update
LSA = Router : 1.1.1.1: R1 : 20 + content
LSA = Router : 9.9.9.9 : R9 : 14 + content
Link-State Acknowledgement
LSA-header = Router : 1.1.1.1: R1 : 20
LSA-header = Router : 9.9.9.9 : R9 : 14
Adjacency just came up

## Slide 16: Each router has link-state database (LSDB)
R5 Link state database
R7 LSP
R9 LSP
R8 LSP
R1 LSP
R3 LSP
R2 LSP
R4 LSP
R6 LSP
R5 LSP
R1
R2
R3
R4
R5
R6
R7
R8
R9
R4
R1
R4
R5
R6
R2
R5
R6
R3
R2
R5
R7
R4
R2
R3
R4
R8
R5
R3
R8
R9
R6
R4
R8
R7
R5
R7
R9
R8
R6
R8
R9

## Slide 17: Construct topology from link-state database
R5 Link state database
R7 LSP
R9 LSP
R8 LSP
R1 LSP
R3 LSP
R2 LSP
R4 LSP
R6 LSP
R5 LSP
R7 LSP
R9 LSP
R8 LSP
R1 LSP
R3 LSP
R2 LSP
R4 LSP
R6 LSP
R5 LSP
R1
R2
R3
R4
R5
R6
R7
R8
R9
R4
R1
R4
R5
R6
R2
R5
R6
R3
R2
R5
R7
R4
R2
R3
R4
R8
R5
R3
R8
R9
R6
R4
R8
R7
R5
R7
R9
R8
R6
R8
R9
R1
R2
R3
R4
R5
R6
R7
R8
R9

## Slide 18: Lessons for quantum networks
Quantum Networks contains both classical links and quantum links
The classical topology and the quantum topology may be different
These existing protocols already have multi-topology extensions
It makes sense to use / generalize OSPF or ISIS for topology discovery in Quantum Networks

## Slide 19: Resources discovery
RSVP / Segment routing
Resource reservation protocol
ISIS-TE / OSPF-TE
Intermediate System to Intermediate System or Open Shortest Path First with Traffic Engineering Extensions
Network topology
Available resources
Traffic demand
Other constraints
Optimal routes for paths
NetFlow / IPFIX
Manual configuration
CSPF
Distributed Constrained Shortest Path First
or
PCE
Centralized Path Computation Element
(G)MPLS
(Generalized) Multi-Protocol Label Switching

## Slide 20: Available bandwidth on every link
E6
E1
E2
E5
E4
E3
C2
C1
C4
C3
Physical bandwidth | 400 Gbps
Reserved bandwidth | 180 Gbps
Available bandwidth | 220 Gbps

## Slide 21: Other resources
In classical networks, link bandwidth is the most important resource
  Link bandwidth is tracked separately for each traffic priority
  Router throughput is usually limited by the links (“non-blocking”)
Administrative group (“color”) for each link
  This is a high latency (satellite link)
  The country in which the link is located (Canada, US, …)
Shared Risk Link Group (SRLG)
  This link is in the same physical conduit as those other links

## Slide 22: Discovery of resources: OSPF-TE or ISIS-TE
Traffic Engineering (TE) extensions to link-state routing protocols: OSPF and ISIS
E6
E1
E2
E5
E4
E3
C2
C1
C4
C3
Traffic engineering attributes of leak link:
Traffic engineering metric
Maximum bandwidth
Maximum reservable bandwidth
Unreserved bandwidth
Administrative group (aka class or color)
Each node floods information about resource availability across the whole network:

## Slide 23: Topology discovery lessons for quantum networks
Classical networks use Traffic Engineering extensions to OSPF or ISIS to flood information about resource availability in the network.
There are new types of network resources that are unique to quantum networks (Bell pairs per second, number of memory qubits, non-deterministic swap success probability, …)
It makes sense to use / generalize OSPF-TE or ISIS-TE for resource discovery in Quantum Networks
This work has already started: IETF draft “Advertising Entanglement Capabilities in Quantum Networks” https://datatracker.ietf.org/doc/draft-kaws-qirg-advent/

## Slide 24: Traffic demand and constraints discovery
RSVP / Segment routing
Resource reservation protocol
ISIS-TE / OSPF-TE
Intermediate System to Intermediate System or Open Shortest Path First with Traffic Engineering Extensions
Network topology
Available resources
Traffic demand
Other constraints
Optimal routes for paths
NetFlow / IPFIX
Manual configuration
CSPF
Distributed Constrained Shortest Path First
or
PCE
Centralized Path Computation Element
(G)MPLS
(Generalized) Multi-Protocol Label Switching

## Slide 25: Traffic demand matrix
E6
E1
E2
E5
E4
E3
C2
C1
C4
C3
Ingress | Egress | Demand
E1 | E2 | 120 Gbps
E1 | E3 | 30 Gbps
E1 | E4 | 20 Gbps
E1 | E5 | 20 Gbps
E1 | E6 | 90 Gbps
E2 | E1 | 40 Gbps
E2 | E3 | 190 Gbps
E2 | E4 | 80 Gbps
E2 | E5 | 70 Gbps
E2 | E6 | 30 Gbps
… | … | …
Traffic demand matrix is typically measured (e.g. using NetFlow or IPFIX)

## Slide 26: How to determine the traffic demand?
Measure demand
  Using NetFlow, IPFIX, etc.
  Take peak demand for diurnal patterns
  Adjust for expected changes
Schedule demand
  Have list of jobs to be completed (e.g. huge file transfers)
  Each job has known bandwidth demand and deadline
  Schedule jobs to meet deadline and maximize network utilization

## Slide 27: Additional constraints
Example use cases:
  Primary LSP and backup LSP must use node-disjoint or link-disjoint paths
  Traffic between Canadian cities cannot go through USA
  Traffic must not use high-latency satellite links
  Traffic must avoid router which is known to need scheduled maintenance
  Etc.
RSVP-TE uses link “colors” for this purpose
Centralized controllers can handle more sophisticated constraints

## Slide 28: Specify path requirements: configuration
Configure path requirements on the ingress node (head) of the path
protocols {
mpls {
label-switched-path my-lsp {
to 10.0.9.7;
bandwidth 100m;
exclude [ satellite-links ];
include [ usa-links canada-links ];
}
}
}

## Slide 29: Demand discovery lessons for quantum networks
If we want to use traffic engineering in quantum networks, we need to know the quantum “demand matrix”:
  How many end-to-end Bell pairs per second (BPPS) between end-points?
  What is the required fidelity of those Bell pairs (similar to QoS in classical networks).
The applications can specify the demand when they request a path (integrated services model).
We can use and out-of-band method to create a demand matrix for the aggregate of all quantum flows (differentiated services model).
The bandwidth of initial quantum networks will be so scarce that the integrated services model makes sense (Even though the classical Internet has abandoned the integrated services model and only uses the differentiated services model now.)

## Slide 30: Path computation
RSVP / Segment routing
Resource reservation protocol
ISIS-TE / OSPF-TE
Intermediate System to Intermediate System or Open Shortest Path First with Traffic Engineering Extensions
Network topology
Available resources
Traffic demand
Other constraints
Optimal routes for paths
NetFlow / IPFIX
Manual configuration
CSPF
Distributed Constrained Shortest Path First
or
PCE
Centralized Path Computation Element
(G)MPLS
(Generalized) Multi-Protocol Label Switching

## Slide 31: Path computation
E6
E1
E2
E5
E4
E3
C2
C1
C4
C3
Given:
Required bandwidth for path
Other constraints
Available bandwidth on each link
Other resource attributes
Do the following:
Compute the best route of the path
Signal the path in the network
Program the path into the forwarding plane

## Slide 32: Distributed algorithm: Constrained SPF (CSPF)
Remove links from topology that do not satisfy constraints
Bandwidth < 100 mbps
Remove “satellite” links
Remove all links outside “usa” or “canada”
E6
E1
E2
E5
E4
E3
C2
C1
C4
C3
Full information in link-state database: all links
E6
E1
E2
E5
E4
E3
C2
C1
C4
C3
Pruned information in link-state database: only links that satisfy constraints
E6
E1
E2
E5
E4
E3
C2
C1
C4
C3
Computed shortest path on remaining topology:
E1→C1 →C3 →C4 →E3

## Slide 33: Centralization of path computation
Path Computation
Engine
SDN controller
Path Computation | Distributed | Centralized | Centralized
Path Signaling | Distributed | Distributed | Path not signaled
Program forwarding plane | Distributed | Distributed | Centralized

## Slide 34: Path computation lessons for quantum networks
General concept of path computation applies to quantum networks
Path computation is more complex in quantum networks
  Limited number of memory qubits
  Non-deterministic swaps
  Distillation
  Etc.
New path computation algorithms and heuristics will be needed.
Logically centralized path computation element makes sense.

## Slide 35: Data plan for traffic engineered networks
RSVP / Segment routing
Resource reservation protocol
ISIS-TE / OSPF-TE
Intermediate System to Intermediate System or Open Shortest Path First with Traffic Engineering Extensions
Network topology
Available resources
Traffic demand
Other constraints
Optimal routes for paths
NetFlow / IPFIX
Manual configuration
CSPF
Distributed Constrained Shortest Path First
or
PCE
Centralized Path Computation Element
(G)MPLS
(Generalized) Multi-Protocol Label Switching

## Slide 36: Difficult to traffic engineer with IP alone
Router
R1
Router
R3
Router
R5
Router
R4
Router
R2
Router
R6
Router
R7
Router
R8
IP forwarding table cannot have two different routes that depend on the source IP address for the same destination IP address.

## Slide 37: Multi-Protocol Label Switching (MPLS)
A new data plane protocol that uses “MPLS labels”
Used to create Label Switched Paths (LSPs)
Enables Traffic Engineering (TE) and many other services
Routers that support MPLS are called Label Switched Routers (LSRs)
MPLS runs over any layer 2 protocol (not just Ethernet)
Any protocol can run over MPLS (not just layer 3 but also layer 2)
Referred to as a layer 2½ protocol
Works with many control plane protocols (RSVP, LDP, BGP, SDN, …)

## Slide 38: MPLS header
Ethernet Header
MPLS Header
IP Packet
Label
Traffic Class
Bottom of Stack
Time to Live
8 bits
1 bit
3 bits
20 bits
4 bytes

## Slide 39: MPLS label switching
R1
R2
R3
R4
IP | Next-hop
1.1.0.0/8 | Push 99, R2
Label | Next-hop
MPLS forwarding table
IP forwarding table
IP | Next-hop
Label | Next-hop
99 | Swap 75, R3
MPLS forwarding table
IP forwarding table
IP | Next-hop
Label | Next-hop
75 | Swap 83, R4
MPLS forwarding table
IP forwarding table
IP | Next-hop
1.1.0.0/8 | R5
Label | Next-hop
83 | Pop
MPLS forwarding table
IP forwarding table
99
1.1.1.1
75
1.1.1.1
83
1.1.1.1
1.1.1.1
1.1.1.1
MPLS Label Switched Path (LSP)
MPLS
IP
MPLS
IP
MPLS
IP
IP
IP

## Slide 40: Penultimate Hop Popping (PHP)
R1
R2
R3
R4
IP | Next-hop
1.1.0.0/8 | Push 99, R2
Label | Next-hop
MPLS forwarding table
IP forwarding table
MPLS forwarding table
IP forwarding table
IP | Next-hop
Label | Next-hop
75 | Pop, R4
MPLS forwarding table
IP forwarding table
IP | Next-hop
1.1.0.0/8 | R5
Label | Next-hop
MPLS forwarding table
IP forwarding table
99
1.1.1.1
75
1.1.1.1
1.1.1.1
1.1.1.1
1.1.1.1
MPLS Label Switched Path (LSP)
MPLS
IP
MPLS
IP
IP
IP
IP
IP | Next-hop
Label | Next-hop
99 | Swap 75, R3

## Slide 41: MPLS Label Stacking
Ethernet
Header
MPLS
Header
IP
Packet
MPLS
Header
MPLS
Header
Top label
(= outer-most label)
Bottom label
(= inner-most label)
MPLS label stack of depth 3
Dest Ethernet Address
a8:66:7f:3a:2b:1a
MPLS label
99
Dest IP Address
1.1.1.1
MPLS label
103
MPLS label
75

## Slide 42: Complex services using simple building blocks Traffic Engineering (TE)
R1
R3
R5
R4
R2
R6
R7
R8
100
1.1.1.1
101
1.1.1.1
102
1.1.1.1
103
1.1.1.1
200
1.1.1.1
201
1.1.1.1
203
1.1.1.1
204
1.1.1.1
202
1.1.1.1
1.1.1.1 → Push 100, R3
100 → Swap 101, R5
101 → Swap 102, R7
102 → Push 103, R8
103 → Pop
1.1.1.1 → Push 200, R3
200 → Swap 201, R4
201 → Swap 202, R6
203 → Push 204, R8
204 → Pop
202 → Swap 203, R7

## Slide 43: Complex services using simple building blocks Fast Re-Route (FRR)
R1
R2
R3
R4
R5
R6
1.1.1.1
100
101
1.1.1.1
1.1.1.1
102
1.1.1.1 → Push 100, R2
100 → Swap 101, R3 (if link to R3 up)
Swap 101, Push 200, R4 (if link to R3 down)
101 → Swap 102, R4
102 → Pop
200 → Swap 201, R6
201→ Pop, R3
Protected LSP
Protection LSP for link R2-R3

## Slide 44: Complex services using simple building blocks Fast Re-Route (FRR)
R1
R2
R3
R4
R5
R6
1.1.1.1
100
1.1.1.1
102
1.1.1.1 → Push 100, R2
100 → Swap 101, R3 (if link to R3 up)
Swap 101, Push 200, R4 (if link to R3 down)
101 → Swap 102, R4
102 → Pop
200 → Swap 201, R6
201→ Pop, R3
Protected LSP
Protection LSP for link R2-R3
Failure
101
1.1.1.1
200
101
1.1.1.1
201
101
1.1.1.1

## Slide 45: Complex services using simple building blocks Pseudo Wire (PW)
R1
R3
R2
Frame
Relay
Switch 1
Frame
Relay
Switch 2
Allows service provider to offer Frame Relay service without a Frame Relay network
Frame Relay
100
Frame Relay
Frame Relay
101
Frame Relay
FR interface 1
FR interface 2
Interface 1 → Push 100, R2
100 → Swap 101, R3
101 → Pop, Interface 2

## Slide 46: Complex services using simple building blocks MPLS Virtual Private Networks (VPNs)
PE-1
PE-2
P
CE-A1
FR interface 1
CE-B1
CE-A2
CE-B2
VRF
A
VRF
B
VRF
A
VRF
B
VPN A
VPN B
1.1.1.1
2.2.2.2
1.1.1.1
2.2.2.2
100
1.1.1.1
200
100
1.1.1.1
201
1.1.1.1
1.1.1.1
2.2.2.2 → Push 100, 200, P
200 → Swap 201, PE-2
201 → Pop, VRF A
2.2.2.2 → CE-A2
VPNs must be isolated and can have overlapping IP address spaces

## Slide 47: Complex services using simple building blocks Segment Routing (SR)
R2
R1
R5
R7
R10
R9
R4
R3
R8
R6
100
1.1.1.1
104
105
104
100 → Pop
101 → Pop, R3
102 → Pop, R4
100 → Pop
101 → Pop, R1
102 → Pop, R2
103 → Pop, R4
104 → Pop, R6
105 → Pop, R7
100 → Pop
101 → Pop, R2
102 → Pop, R3
103 → Pop, R4
104 → Pop, R7
105→ Pop, R8
100 → Pop
101 → Pop, R4
102 → Pop, R6
103 → Pop, R9
104 → Pop, R10
100 → Pop
101 → Pop, R6
102 → Pop, R8
1.1.1.1 → Push 104, 105, 104, 100
100
1.1.1.1
104
105
100
1.1.1.1
104
100
1.1.1.1
Sender encodes path into packet.
No path signaling required.
Less state in routers:
O(#neighbors)
Instead of
O(#paths)

## Slide 48: Generalized MPLS (GMPLS)
Generalization of MPLS when data plane cannot carry explicit labels
Instead the label is implicit
OXC: Optical port is implicit label
ROADM: Wavelength is implicit label
SONET ADM: TDM timeslot is implicit label

## Slide 49: Data-plane lessons for quantum networks
The data plane should use very simple but flexible primitives Just like MPLS push, swap, pop
That support many different services Just like MPLS TE, FRR, PW, VPN, SR, …
That are independent of the signaling protocol Just like MPLS is independent of RSVP, LDP, BGP, …
That don’t assume that data plane can carry control headers Just like GMPLS Qubits don’t have headers; need some implicit label (e.g. timeslot)
The quantum data plane will need to be stateful Unlike IP and MPLS which are stateless Needed because the creation of a single end-to-end Bell pair is a stateful multi-step process: multiple point-to-point Bell pairs, distillation, swaps, etc.
Proposal: use P4 and add quantum and statefulness extensions In research phase, quantum protocols will change often

## Slide 50: Signaling protocol for traffic engineered paths
RSVP / Segment routing
Resource reservation protocol
ISIS-TE / OSPF-TE
Intermediate System to Intermediate System or Open Shortest Path First with Traffic Engineering Extensions
Network topology
Available resources
Traffic demand
Other constraints
Optimal routes for paths
NetFlow / IPFIX
Manual configuration
CSPF
Distributed Constrained Shortest Path First
or
PCE
Centralized Path Computation Element
(G)MPLS
(Generalized) Multi-Protocol Label Switching

## Slide 51: MPLS signaling protocols
Resource reservation protocol with traffic engineering extensions (RSVP-TE)
Label distribution protocol (LDP)
Targeted label distribution protocol (T-LDP)
Border gateway protocol labeled unicast (BGP-LU)
Border gateway protocol layer 3 virtual private networks (BGP L3VPN)
Border gateway protocol layer 2 virtual private networks (BGP L2VPN)
Border gateway protocol layer ethernet virtual private networks (BGP EVPN)
Border gateway protocol labeled unicast (BGP LU)
OpenFlow

## Slide 52: Label allocation concepts
Downstream vs upstream
On-demand vs unsolicited
Ordered vs unordered
Conservative vs liberal retention

## Slide 53: Resource reservation protocol (RSVP-TE)
RSVP was originally designed for integrated services (IntServ) Bandwidth reservation for individual flows of traffic
RSVP-TE is currently used for differentiated services (DiffServ) Strategic / tactical bandwidth reservation of aggregates of many flows
Relies on OSPF-TE or ISIS-TE for path computation
Relies on MPLS or GMPLS for data plane
Uses downstream-on-demand label allocation with conservative retention mode

## Slide 54: RSVP path signaling
R1
R2
R3
R4

## Slide 55: RSVP path signaling
R1
R2
R3
R4
Reserve requested bandwidth
Allocate label 100
PATH
ERO = R2,R3,R4
requested bandwidth = 1 Gbps
ERO = Explicit Route Object (route computed by path computation function)

## Slide 56: RSVP path signaling
R1
R2
R3
R4
Reserve requested bandwidth
Allocate label 101
PATH
ERO = R2,R3,R4
requested bandwidth = 1 Gbps

## Slide 57: RSVP path signaling
R1
R2
R3
R4
Reserve requested bandwidth
Allocate label 102
PATH
ERO = R2,R3,R4
requested bandwidth = 1 Gbps

## Slide 58: RSVP path signaling
R1
R2
R3
R4
RESV
label = 102
Install MPLS route 102 → Pop

## Slide 59: RSVP path signaling
R1
R2
R3
R4
RESV
label = 101
Install MPLS route 101 → Swap 102, R4

## Slide 60: RSVP path signaling
R1
R2
R3
R4
RESV
label = 100
Install MPLS route 100 → Swap 101, R3

## Slide 61: RSVP is soft state (needs periodic refresh)
R1
R2
R3
R4
PATH-refresh
PATH-refresh
PATH-refresh
RESV-refresh
RESV-refresh
RESV-refresh
PATH-refresh
PATH-refresh
RESV-refresh
RESV-refresh
RESV-refresh
PATH-refresh

## Slide 62: LSP installed by LSP signalling
R1
R2
R3
R4
x.x.x.x
100
101
x.x.x.x
x.x.x.x
102
x.x.x.x → Push 100, R2
101 → Swap 102, R4
102 → Pop
100 → Swap 101, R3
This route is not installed by RSVP, but by some protocol that decides to ”use” the LSP

## Slide 63: Some notes on bandwidth reservations
Reservation of the bandwidth is only a matter of control-plan “book keeping”.
RSVP itself typically does not install any rate limiters or shapers in the data plane
RSVP only makes sure the traffic will fit if the demand actually matches the reservations
Typically “other mechanisms” are used to rate limit or shape the traffic that goes into LSPs
Or, alternatively, ”auto-bandwidth” is used to grow or shrink the LSPs according to the actual demand

## Slide 64: Challenges with RSVP
Traffic engineer full mesh of LSPs between edge routers Based on traffic demand matrix
N edge routers require N2 LSPs 100 edge routers means 10,000 LSPs Core routers may have 10,000 transit LSPs
High RSVP signaling load in control plane Initial signaling Refresh signaling
Large amount of state in forwarding plane N2 MPLS routes

## Slide 65: Possible solutions to RSVP challenges
Reduce scope of traffic engineering Reduce N in N2 Only traffic engineer the core of the core Run LDP-over-RSVP edge-to-edge
RSVP refresh reduction Various mechanisms to reduce the amount refresh messages Personally I liked CR-LDP which is hard-state (lost the race due to non-technical reasons)
Use Segment Routing (SR) Less state in control and data plane: label per neighbor instead of label per path More state in packet (introduces problems of its own due to hardware limitations) No signaling of LSPs Puts much more control in the hands of the applications

## Slide 66: Signaling lessons for quantum networks
We already decided that a centralized path computation element makes sense for quantum networks.
In that case, we can initially do without a router-to-router signaling protocol such as RSVP.
Instead, we can use a controller-to-router protocol (e.g. a generalization of PCEP or P4 APIs)
We can always add a generalization of RSVP or SR later

## Slide 67: Summary of lessons for quantum networks
Traffic engineering makes sense for quantum networks
Existing classical protocols can be re-used and/or generalized for quantum networks:
  Topology discovery: use OSPF or ISIS multi-topology
  Resource discovery: generalize TE extensions for OSPF or ISIS and introduce new types of resources (already work-in-progress)
  Path computation: use centralized path computation engine and develop new path computation algorithms that are aware of the specifics of quantum repeaters (just started an open source project on GitHub)
  Path signaling: at first use SDN approach that eliminates the need for a router-to-router signaling protocol. Later potentially generalize RSVP-TE or SR.
  Forwarding plane: use existing mechanisms (e.g. P4) for classical messages, develop new (stateful) primitives for quantum qubits

## Slide 68
Thank you!