## Slide 1: Protocol Design Considerations
Version 1, Presented at QuTech (Delft) on 22 November 2019

## Slide 2: Multi-version, multi-vendor, multi-feature. The Internet is an uncontrolled mixture of devices from different vendors running different versions of code which support different combinations of features.

## Slide 3: Interop between protocol versions
Version X needs to interoperate with version Y.
For any X and Y, not just Y = X + 1.
Don’t assume contiguous “regions” of same version.
Different devices will run different version of your protocol.
Temporarily during upgrade. You cannot upgrade your devices all at once; it takes a lot of time.
Or semi-permanently due to operational considerations (e.g. different vendors support different versions of the protocol). You want to be able to have multiple vendors in the same network.
Version 1
Version 2
Version 1
Version 1
Version 3

## Slide 4: Lessons learned from major version bumps
IPv4 vs IPv6
  IPv6 is not backwards compatible with IPv4
  Upgrading from IPv4 to IPv6 is a royal pain in the neck
  It’s been 20 years and IPv6 is still not universally deployed
  IPv4 will never go away
OSPFv3 vs OSPFv2
  OSPFv3 is not backwards compatible with OSPFv2
  You need to upgrade from OSPFv2 to OSPFv3 to get IPv6
  Real networks run OSPFv2 and OSPFv3
  ISIS did it right (ISIS with IPv6 can interoperate with ISIS without IPv6)
BGPv3 vs BGPv4 vs …BGPv5?
  BGPv3 is not backwards compatible with BGPv4, it required every Internet core router to be upgraded
  Upgrading every core router on the Internet is infeasible at this time
  BGPv4 has excellent extension mechanisms; it is unlikely that there will ever be a BGPv5

## Slide 5: Interop between feature sets
Protocol implementation that has feature A must interoperate with protocol implementation that does not have feature A.
Different vendors and versions of code have different feature sets.
Don’t assume the feature set can be derived from the protocol version. Allows protocol extensions to evolve and be deployed independently.
Don’t assume the feature set is the same. Feature set A+B must interoperate with B+C.
A
B
C
D
Protocol features
A
A
A
B
B
B
C
C
C
D
D
D

## Slide 6: Capability announcement (“negotiation”)
I support features B, C, D
We can use features B, C (these are the ones we have in common)
A
B
C
B
C
D
I support features A, C, D
We can use features B, C (these are the ones we have in common)
(Things get a bit more complicated when more than 2 devices are involved, e.g. flooding)

## Slide 7: Example: BGPv4 capabilities

## Slide 8: Type Length Value (TLV) Encoding

## Slide 9: Transitive bits

## Slide 10: Crashes and planned upgrades. There is no such thing as a maintenance window on the Internet.

## Slide 11: Chassis devices
Everything (routing engine, switch fabric, power supplies, fans, …) redundant and in-service replaceable
Redundant control planes (routing engines)

## Slide 12: In-Service Software Upgrade (ISSU)
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 1
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 2
Standby routing engine:
Version 2
Upgrade
standby
Switch-over
Upgrade
new standby

## Slide 13: Non-Stop Forwarding (NSF) Also known as Graceful Restart (GR)
Forwarding engine STALE TABLES
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESYNCHRONIZE
Control-plane session RESYNCHRONIZE
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESTART FINISHED
Control-plane session RESTART FINISHED
Data-plane traffic
Data-plane traffic
Control-plane session
PREPARE FOR RESTART
Control-plane session PREPARE FOR RESTART

## Slide 14: Pizza-box devices
Does not have redundant routing hardware routing engines.
(Sometimes in redundant software routing engines using virtual machines or containers.)

## Slide 15: Non-Stop Routing (NSR)

## Slide 16: Scale-out instead of scale-up

## Slide 17: Relatively small impact of losing one device
For planned upgrades, announce in advance (e.g. overload flag) to shift traffic away, if possible.

## Slide 18: Soft state does not scale. Periodic protocols do not scale. Use hard state instead.

## Slide 19: Use existing reliability mechanisms. Don’t invent your own reliability mechanism. Run over a transport when possible.

## Slide 20: You need flow and congestion control. Not just in application protocols, but also in routing and signaling protocols.

## Slide 21: Protocol correctness is hard. Much harder than you think.

## Slide 22: 1980: The entire Internet had to be rebooted

## Slide 23: Implementation correctness is hard. Much harder than you think.

## Slide 24: Don’t hand-code your parsers
Type Length Value (TLV) encoding (we saw this before!)
Formal modeling language for on-the-wire protocol
  Abstract Syntax Number 1 (ASN.1)
  YANG
  Google Protocol Buffers (BGP), Thrift, etc.
@@@ Example of real-life bug

## Slide 25: Thank you.

## Slide 26: References
Some lessons from history (“Those who do not know history are doomed to repeat it”) https://datatracker.ietf.org/meeting/102/materials/slides-102-rtgarea-those-who-do-not-learn-history-are-doomed-to-repeat-it-00