## Slide 1: Protocol Design Considerations
Version 1, Presented at QuTech (Delft) on 22 November 2019

## Slide 2: Protocol correctness is hard. Much harder than you think.

## Slide 3: A story The day the entire Internet had to be rebooted due to an OSPF protocol design error.

## Slide 4: Implementation correctness is hard. Much harder than you think.

## Slide 5: A story How a coding mistake in BGP caused routers all over the Internet to crash.

## Slide 6: A story The day the entire Internet had to be rebooted due to a protocol design error.

## Slide 7: Protocol security is hard. Much harder than you think.

## Slide 8: A story How hackers robbed a bitcoin bank using a weakness in BGP

## Slide 9: Flow control Congestion control Error control (reliability) Don’t mix them up: not in your mind and not in your protocol.

## Slide 10: Flow control
Make sure sender does not produce data faster
than receiver can consume them.
Note: here it is the receiver that is not keeping up; the network can keep up fine.
Send 5 packets per second (pps)
Consume 3 pps
Drop 2 pps
Receive buffer overflows.
Buffer can absorb bursts but not sustained rate difference.

## Slide 11: Flow control approaches
General principle: make the data arrive more slowly
Delay-insensitive traffic
  It is okay to receive data later
  Web pages, file transfer, e-mail, …
  Receiver makes the sender slow down
  Requires ability to back-pressure sending application to send data slower
  Typical approach: sliding window (e.g. spinner waiting to load webpage)
Delay-sensitive traffic
  It is not okay to receive data later
  Voice, live video, video on demand, …
  Receiver makes the send send less data
  Requires ability to back-pressure sending application to send less data
  Typical approach: adaptive encoding (e.g. fuzzy video in Netflix)

## Slide 12: Flow control in quantum network
Make sure sender does not produce qubits faster
than receiver can consume them.

## Slide 13: Wavy line

## Slide 14: Congestion control
Make sure senders do not produce data faster
than network can carry it.
Send link-rate
Send link-rate
Try to send 2x link-rate traffic on link.
Transmit buffer overflows.
Drop half of traffic.

## Slide 15: Active Queue Management (AQM)
Decide which packet to service next in the send queue
  Classification: @@@
  Hierarchical schedulers: @@@
  Shapers: @@@
Decide when to start dropping packets
  Tail-drop
  Random Early Drop (RED)
Decide which packet to drop
  In-profile vs out-of-profile

## Slide 16: Hierarchical queue scheduler
Source https://www.juniper.net/documentation/en_US/junos/information-products/pathway-pages/cos/config-guide-hierarchical-cos.pdf

## Slide 17: Congestion control approaches
General principle: send traffic more slowly when congestion occurs
Detect dropped packets at transport layer and reduce window
  TCP slow start algorithm
  Extremely difficult to ”get right” (TCP Reno, Vegas, high speed, BIC, CUBIC, C2TCP, NATCP, Elastic TCP, and many many more variations)
  Assumes everyone “plays fair”
Backwards Explicit Congestion Notification (BECN)
  @@@
Forward Explicit Congestion Notification (FECN)
  Set bits in forwarded IP packet: Congestion Encountered (CE)
  Requires cooperation from the transport layer to slow down

## Slide 18: Flow control
Make sure sender does not produce data faster
than receiver can consume them.
Note: here it is the receiver that is not keeping up; the network can keep up fine.
Send 5 packets per second (pps)
Consume 3 pps
Drop 2 pps
Receive buffer overflows.
Buffer can absorb bursts but not sustained rate difference.

## Slide 19: Mixing up flow, congestion and error control
@@@ bad idea @@@

## Slide 20: Multi-version, multi-vendor, multi-feature. The Internet is an uncontrolled mixture of devices from different vendors running different versions of code which support different combinations of features.

## Slide 21: Interop between protocol versions
Version X needs to interoperate with version Y.
For any X and Y, not just Y = X + 1.
Don’t assume contiguous “regions” of same version.
Different devices will run different version of your protocol.
Temporarily during upgrade. You cannot upgrade your devices all at once; it takes a lot of time.
Or semi-permanently due to operational considerations (e.g. different vendors support different versions of the protocol). You want to be able to have multiple vendors in the same network.
Version 1
Version 2
Version 1
Version 1
Version 3

## Slide 22: Lessons learned from major version bumps
IPv4 vs IPv6
  IPv6 is not backwards compatible with IPv4
  Upgrading from IPv4 to IPv6 is a royal pain in the neck
  It’s been 20 years and IPv6 is still not universally deployed
  IPv4 will never go away
OSPFv3 vs OSPFv2
  OSPFv3 is not backwards compatible with OSPFv2
  You need to upgrade from OSPFv2 to OSPFv3 to get IPv6
  Real networks run OSPFv2 and OSPFv3
  ISIS did it right (ISIS with IPv6 can interoperate with ISIS without IPv6)
BGPv3 vs BGPv4 vs …BGPv5?
  BGPv3 is not backwards compatible with BGPv4, it required every Internet core router to be upgraded
  Upgrading every core router on the Internet is infeasible at this time
  BGPv4 has excellent extension mechanisms; it is unlikely that there will ever be a BGPv5

## Slide 23: Interop between feature sets
Protocol implementation that has feature A must interoperate with protocol implementation that does not have feature A.
Different vendors and versions of code have different feature sets.
Don’t assume the feature set can be derived from the protocol version. Allows protocol extensions to evolve and be deployed independently.
Don’t assume the feature set is the same. Feature set A+B must interoperate with B+C.
A
B
C
D
Protocol features
A
A
A
B
B
B
C
C
C
D
D
D

## Slide 24: Capability announcement (“negotiation”)
I support features B, C, D
We can use features B, C (these are the ones we have in common)
A
B
C
B
C
D
I support features A, C, D
We can use features B, C (these are the ones we have in common)
(Things get a bit more complicated when more than 2 devices are involved, e.g. flooding)

## Slide 25: Example: BGPv4 capabilities

## Slide 26: Type Length Value (TLV) Encoding

## Slide 27: How to handle unrecognized TLVs?
What should you do when you receive a TLV with an unknown type?
Happens when another device is running a newer version of the protocol.
Options:
  Ignore and propagate the TLV
  Ignore and remove the TLV
  Declare an error
  Note: ignoring is possible because the length L is known and the value can be skipped
The originator of the TLV (who by definition understands it) sets some extra bits in the TLV to instruct the receiver what to do.

## Slide 28: Example: Label Distribution Protocol (LDP)
TLV encoding is also used in:
BGP
OSPF
ISIS
RSVP
Many more…

## Slide 29: Crashes and planned upgrades. There is no such thing as a maintenance window on the Internet.

## Slide 30: Chassis devices
Everything (routing engine, switch fabric, power supplies, fans, …) redundant and in-service replaceable
Redundant control planes (routing engines)

## Slide 31: In-Service Software Upgrade (ISSU)
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 1
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 2
Standby routing engine:
Version 2
Upgrade
standby
Switch-over
Upgrade
new standby

## Slide 32: Non-Stop Forwarding (NSF) Also known as Graceful Restart (GR)
Forwarding engine STALE TABLES
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESYNCHRONIZE
Control-plane session RESYNCHRONIZE
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESTART FINISHED
Control-plane session RESTART FINISHED
Data-plane traffic
Data-plane traffic
Control-plane session
PREPARE FOR RESTART
Control-plane session PREPARE FOR RESTART

## Slide 33: Pizza-box devices
Does not have redundant routing hardware routing engines.
(Sometimes in redundant software routing engines using virtual machines or containers.)

## Slide 34: Non-Stop Routing (NSR)

## Slide 35: Scale-out instead of scale-up

## Slide 36: Relatively small impact of losing one device
For planned upgrades, announce in advance (e.g. overload flag) to shift traffic away, if possible.

## Slide 37: Soft state does not scale. Periodic protocols do not scale. Use hard state instead.

## Slide 38: Soft state vs hard state
Soft state protocol
A.k.a. Periodic protocol
Sender initially sends data.
Receiver puts data in its database.
Sender periodically resends data.
If receiver doesn’t receive data anymore, it removes data from its database after time-out.
Heavy load due to periodic transmission.
Fallacy: simpler cleanup when sender crashes.
Sender wants to advertise some data (e.g. a route) to receiver.
Hard state state protocol
Runs protocol over reliable transport connection.
Sender initially sends data.
Receiver puts data in its database.
No periodic re-transmissions of data.
Receiver keep data in database until (a) sender explicitly withdraws data or (b) transport connection is disconnected.
No traffic if no changes in the database.
Needs reliable transport connection and keep-alive mechanism.

## Slide 39: Use existing reliability mechanisms. Don’t invent your own reliability mechanism. Run over a transport when possible.

## Slide 40: You need flow and congestion control. Not just in application protocols, but also in routing and signaling protocols.

## Slide 41: Protocol correctness is hard. Much harder than you think.

## Slide 42: 1980: The entire Internet had to be rebooted

## Slide 43: Packet replication loops
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast) +
Forwarding loop
=
Network meltdown
Due to explosion of traffic

## Slide 44: Packet replication loops
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast) +
Forwarding loop
+
Absence of TTL mechanism
Packets can loop forever without TTL expiring
=
Disastrous nearly unfixable network meltdown
Due to explosion of traffic which doesn’t go away, even after you shut up the source

## Slide 45: Example: Ethernet address learning + SPT
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast) +
Forwarding loop
=
Network meltdown
Due to explosion of traffic

## Slide 46: Triggered state machine loops

## Slide 47: Implementation correctness is hard. Much harder than you think.

## Slide 48: Don’t hand-code your parsers
Type Length Value (TLV) encoding (we saw this before!)
Formal modeling language for on-the-wire protocol
  Abstract Syntax Number 1 (ASN.1)
  YANG
  Google Protocol Buffers (BGP), Thrift, etc.
@@@ Example of real-life bug

## Slide 49: Thank you.

## Slide 50: References
Some lessons from history (“Those who do not know history are doomed to repeat it”) https://datatracker.ietf.org/meeting/102/materials/slides-102-rtgarea-those-who-do-not-learn-history-are-doomed-to-repeat-it-00