## Slide 1: Protocol Design Considerations
Version 1, Presented at QuTech (Delft) on 22 November 2019

## Slide 2: Flow control Congestion control Error control (reliability) Don’t mix them up: not in your mind and not in your protocol.

## Slide 3: Flow control
Make sure sender does not produce data faster
than receiver can consume them.
Note: here it is the receiver that is not keeping up; the network can keep up fine.
Send 5 packets per second (pps)
Consume 3 pps
Drop 2 pps
Receive buffer overflows.
Buffer can absorb bursts but not sustained rate difference.

## Slide 4: Flow control approaches
General principle: make the data arrive more slowly
Delay-insensitive traffic
  It is okay to receive data later
  Web pages, file transfer, e-mail, …
  Receiver makes the sender slow down
  Requires ability to back-pressure sending application to send data slower
  Typical approach: sliding window (e.g. spinner waiting to load webpage)
Delay-sensitive traffic
  It is not okay to receive data later
  Voice, live video, video on demand, …
  Receiver makes the send send less data
  Requires ability to back-pressure sending application to send less data
  Typical approach: adaptive encoding (e.g. fuzzy video in Netflix)

## Slide 5: Flow control in quantum network
Make sure sender does not produce qubits faster
than receiver can consume them.

## Slide 6: Wavy line

## Slide 7: Congestion control
Make sure senders do not produce data faster
than network can transfer it.

## Slide 8: Flow control approaches
General principle: make the data arrive more slowly
Delay-insensitive traffic
  It is okay to receive data later
  Web pages, file transfer, e-mail, …
  Receiver makes the sender slow down
  Requires ability to back-pressure sending application to send data slower
  Typical approach: sliding window (e.g. spinner waiting to load webpage)
Delay-sensitive traffic
  It is not okay to receive data later
  Voice, live video, video on demand, …
  Receiver makes the send send less data
  Requires ability to back-pressure sending application to send less data
  Typical approach: adaptive encoding (e.g. fuzzy video in Netflix)

## Slide 9: Multi-version, multi-vendor, multi-feature. The Internet is an uncontrolled mixture of devices from different vendors running different versions of code which support different combinations of features.

## Slide 10: Interop between protocol versions
Version X needs to interoperate with version Y.
For any X and Y, not just Y = X + 1.
Don’t assume contiguous “regions” of same version.
Different devices will run different version of your protocol.
Temporarily during upgrade. You cannot upgrade your devices all at once; it takes a lot of time.
Or semi-permanently due to operational considerations (e.g. different vendors support different versions of the protocol). You want to be able to have multiple vendors in the same network.
Version 1
Version 2
Version 1
Version 1
Version 3

## Slide 11: Lessons learned from major version bumps
IPv4 vs IPv6
  IPv6 is not backwards compatible with IPv4
  Upgrading from IPv4 to IPv6 is a royal pain in the neck
  It’s been 20 years and IPv6 is still not universally deployed
  IPv4 will never go away
OSPFv3 vs OSPFv2
  OSPFv3 is not backwards compatible with OSPFv2
  You need to upgrade from OSPFv2 to OSPFv3 to get IPv6
  Real networks run OSPFv2 and OSPFv3
  ISIS did it right (ISIS with IPv6 can interoperate with ISIS without IPv6)
BGPv3 vs BGPv4 vs …BGPv5?
  BGPv3 is not backwards compatible with BGPv4, it required every Internet core router to be upgraded
  Upgrading every core router on the Internet is infeasible at this time
  BGPv4 has excellent extension mechanisms; it is unlikely that there will ever be a BGPv5

## Slide 12: Interop between feature sets
Protocol implementation that has feature A must interoperate with protocol implementation that does not have feature A.
Different vendors and versions of code have different feature sets.
Don’t assume the feature set can be derived from the protocol version. Allows protocol extensions to evolve and be deployed independently.
Don’t assume the feature set is the same. Feature set A+B must interoperate with B+C.
A
B
C
D
Protocol features
A
A
A
B
B
B
C
C
C
D
D
D

## Slide 13: Capability announcement (“negotiation”)
I support features B, C, D
We can use features B, C (these are the ones we have in common)
A
B
C
B
C
D
I support features A, C, D
We can use features B, C (these are the ones we have in common)
(Things get a bit more complicated when more than 2 devices are involved, e.g. flooding)

## Slide 14: Example: BGPv4 capabilities

## Slide 15: Type Length Value (TLV) Encoding

## Slide 16: Transitive bits

## Slide 17: Crashes and planned upgrades. There is no such thing as a maintenance window on the Internet.

## Slide 18: Chassis devices
Everything (routing engine, switch fabric, power supplies, fans, …) redundant and in-service replaceable
Redundant control planes (routing engines)

## Slide 19: In-Service Software Upgrade (ISSU)
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 1
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 2
Standby routing engine:
Version 2
Upgrade
standby
Switch-over
Upgrade
new standby

## Slide 20: Non-Stop Forwarding (NSF) Also known as Graceful Restart (GR)
Forwarding engine STALE TABLES
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESYNCHRONIZE
Control-plane session RESYNCHRONIZE
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESTART FINISHED
Control-plane session RESTART FINISHED
Data-plane traffic
Data-plane traffic
Control-plane session
PREPARE FOR RESTART
Control-plane session PREPARE FOR RESTART

## Slide 21: Pizza-box devices
Does not have redundant routing hardware routing engines.
(Sometimes in redundant software routing engines using virtual machines or containers.)

## Slide 22: Non-Stop Routing (NSR)

## Slide 23: Scale-out instead of scale-up

## Slide 24: Relatively small impact of losing one device
For planned upgrades, announce in advance (e.g. overload flag) to shift traffic away, if possible.

## Slide 25: Soft state does not scale. Periodic protocols do not scale. Use hard state instead.

## Slide 26: Use existing reliability mechanisms. Don’t invent your own reliability mechanism. Run over a transport when possible.

## Slide 27: You need flow and congestion control. Not just in application protocols, but also in routing and signaling protocols.

## Slide 28: Protocol correctness is hard. Much harder than you think.

## Slide 29: 1980: The entire Internet had to be rebooted

## Slide 30: Implementation correctness is hard. Much harder than you think.

## Slide 31: Don’t hand-code your parsers
Type Length Value (TLV) encoding (we saw this before!)
Formal modeling language for on-the-wire protocol
  Abstract Syntax Number 1 (ASN.1)
  YANG
  Google Protocol Buffers (BGP), Thrift, etc.
@@@ Example of real-life bug

## Slide 32: Thank you.

## Slide 33: References
Some lessons from history (“Those who do not know history are doomed to repeat it”) https://datatracker.ietf.org/meeting/102/materials/slides-102-rtgarea-those-who-do-not-learn-history-are-doomed-to-repeat-it-00