## Slide 1: Protocol Design Considerations
Version 1, Presented at QuTech (Delft) on 22 November 2019

## Slide 2: A few true stories…

## Slide 3: Designing correct protocols is hard
On 27 October 1980, all routers in the entire Internet had to be rebooted simultaneously to recover from a protocol design weakness.
http://www.hannaypublications.com/portfolio/wp-content/uploads/2016/02/AppliedComms_A2.pdf

## Slide 4: Version numbers to pick newest message
Message
Version number 8
Message
Version number 40
Message
Version number 44
<
<
Note: this mechanism is still used today, for example in OSPF and ISIS link state flooding
Oldest version
Newest version

## Slide 5: Modulo 64 comparison creates ”version loop”
Version field was unsigned 6-bit integer, so math is modulo 64
Competing message versions kept replacing each other forever, eating up all CPU
The versions were introduced to a double bit error, which was not detected because check-sums were disabled.
Message
Version number 8
Message
Version number 40
Message
Version number 44
8 < 40
(modulo 64)
40 < 44
(modulo 64)
44 < 8
(modulo 64)

## Slide 6: We have not quite yet learned our lessons
A similar problem exists in the BGP specification and is observed in the Internet to this day.
See BGP persistent route oscillations (RFC3345)

## Slide 7: Implementing protocols correctly is hard
A bug in a widely used BGP implementation allowed an attacker to advertise a BGP route that caused many BGP routers on the other side of the world to crash.
Sending a specially constructed 4-octet AS-path caused certain routers to crash CVE-2014-3818 https://securitytracker.com/id/1031009

## Slide 8: Protocol security is hard
A BGP vulnerability enabled hackers to rob a bitcoin bank.
https://www.wired.com/2014/08/isp-bitcoin-theft/

## Slide 9: Flow control Congestion control Error control in the data plane

## Slide 10: Flow control
Make sure the sender does not produce data faster
than the receiver can consume it.
Note: here it is the receiver that is not keeping up; the network can keep up fine.
Send 5 packets per second (pps)
Consume 3 pps
Drop 2 pps
Receive buffer overflows.
Buffer can absorb bursts but not sustained rate difference.

## Slide 11: Flow control in quantum network
Qubit to be teleported
Sender never stores more than one “qubit to be sent” in memory
Qubit that has been teleported
Receiver needs to store it in memory until it is consumed (measured)
Make sure sender does not produce qubits faster
than receiver can consume them.
Bell pair
Ideally, it is produced “fresh” just before we have a qubit to teleport
Consumer can run out of qubit memory ifs sender sends qubits
faster than received consumes (measures) them.
[Animation]

## Slide 12: Flow control approaches
General principle: make the data arrive more slowly
Approach 1: Sliding window
  Receiver makes the sender slow down by delaying permission to send
  It is okay to receive data later (delay in-sensitive traffic)
  Web pages, file transfer, e-mail, …
Approach 2: Adaptive encoding
  The sender sends less data by switching to more lossy compression
  It is not okay to receive data later (delay-sensitive traffic)
  Voice, live video, video on demand, …
Related approach: Time slot scheduling
  Used in Time Division Multiplexing (TDM) and wireless networks
  Avoids congestion from happening in the first place
Sender must be able to back-pressure application

## Slide 13: Sliding window
Window size = 5
Window size = 3
Window size = 2
Window size = 0
Consumed
Buffer size 5

## Slide 14: Bandwidth-delay product
100 Gbps, 5000 km (= 50 ms round-trip @ speed of light in fiber)
Window size must be ≥ bandwidth * round-trip delay to fully utilize available bandwidth.
In this example window size (= receive buffer size) is 100 MB = 800 Mbit
Only 32% of available bandwidth is used.
window size 800 Mbit @
100 Gbps = 8 ms
Round-trip time 25 ms

## Slide 15: Congestion
Make sure senders do not produce data faster
than network can carry it.
Send link-rate
Send link-rate
Try to send 2x link-rate traffic on link.
Transmit buffer overflows.
Drop half of traffic.

## Slide 16: Congestion control
Congestion avoidance: avoid congestion in the first place
Congestion mitigation: deal with congestion when it does occur
Worst case scenario: congestive collapse
  Effective capacity of the network to carry useful traffic drops to zero
  Retransmissions due to excessive drops and queueing delays overwhelm network
  More likely to happen when capacity is low compared to demand (as it will be in early quantum networks!)
  This actually happened in the early internet: in 1986 the capacity collapsed from 32 Kbps to 40 bps (not Kbps) https://blog.acolyer.org/2015/05/21/congestion-avoidance-and-control/ https://tools.ietf.org/html/rfc896

## Slide 17: Congestion avoidance
Congestion avoidance: mechanisms to avoid congestion in the first place
General principle: send traffic more slowly when congestion occurs
TCP congestion control
  TCP tries to estimate maximum rate before congestion occurs
  TCP sender dynamically congestion window based on presence or absence of drops
  Extremely difficult to get right: Reno, Vegas, BIC, CUBIC, …. and many more algorithms
  Assumes everyone plays fair
Backwards Explicit Congestion Notification (BECN)
  Router sends message to source to slow down when it observes congestion
Forward Explicit Congestion Notification (FECN)
  Set bits in forwarded IP packet: Congestion Encountered (CE)
  Requires cooperation from the transport layer to slow down

## Slide 18: Congestion mitigation
Active Queue Management (AQM):
  Mechanism for dealing with congestion when it does occur
  Queueing only happens if there is contention = congestion
Decide which packets are most important
  Classification at the edge
  Mark classification result into QoS / precedence bits in packet header
Decide which packet to service next in the send queue
  Hierarchical schedulers
  Shapers
Decide when to start dropping packets and which packet to drop
  Tail-drop
  Random Early Drop (RED)
  Drop out-of-profile packet before in-profile packets

## Slide 19: Hierarchical queue scheduler
Source https://www.juniper.net/documentation/en_US/junos/information-products/pathway-pages/cos/config-guide-hierarchical-cos.pdf

## Slide 20: “Congestion control” in quantum networks
End-points cannot get more end-to-end Bell pairs per second (Bpps) than network can produce them
based on bottleneck link or router.
10 Bpps
10 Bpps
10 Bpps
10 Bpps
10 Bpps
Desire X Bpps
Desire Y Bpps
Bottleneck link.
Cannot achieve desired end-to-end entanglements if X+Y > 10
(or even less considering non-deterministic swaps and distillation)

## Slide 21: Reliable transport: error detection and recovery
This is an example of the go-back-N error recovery
1
2
3
4
Time-out
waiting for akc-2
based on estimate RTT
Retransmit packets +
Adjust congestion window
2
3
Retransmit
Retransmit
4
Retransmit
Ack 1
Ack 2
Ack 3
Dropped
(most likely due to congestion)

## Slide 22: Error detection and recovery mechanisms
Checksums
  To detect transmission errors
  Classical networks are so reliable that the vast majority of drops are due to congestion
Automatic Repeat Request (ARQ)
  Receiver sends an acknowledgement (ack) when it has correctly received the data
  The sender re-transmits the data when it does not receive the ack
  Not an option for quantum networks (requires that the sender keeps a copy until the data is acknowledged, in case the data needs to be retransmitted).
  Go-back-N: resend all data starting at the dropped packet
  Selective repeat: only resend the data that was dropped (requires selective ack)
Forward Error Correction (FEC)
  When error rate is too high (noisy links)
  When retransmission is delay is not acceptable (e.g. long latency satellite links)
  The only option in quantum networks (quantum error correcting codes)

## Slide 23: What is so difficult about this?
Flow control, congestion control, and error control are separate but closely related concepts
Most transport protocols don’t have clean separation of concerns
For example, in TCP absence of ACK can mean many things:
  Flow control: receiver wants us to slow down
  Error: data packet or ACK was dropped
  Congestion: data packet or ACK was delayed in queue
Over time TCP has been enhanced:
  Selective acknowledgement (SACK)
  Timestamps

## Slide 24: Flow control Congestion control Error control in the control plane

## Slide 25: Flow control matters in the control plane
Routing and signaling protocols exchange large volumes of data
Sender must not overwhelm receiver
Flow control approaches in routing and signaling protocols:
  Fixed pacing
  Flow control mechanism built into the protocol itself
  Rely on TCP flow control

## Slide 26: Example: ISIS flow control
IIH
Initial database synchronization sends large volume of link state packets (LSPs) Potentially tens of thousands of LSPs
LSP
ISIS adjacency comes up
Initial link-state database (LSDB) synchronization
Pacing parameters in standard, e.g. minimumLSPTransmissionInterval
Recent proposals to dynamically control intervals in ISIS protocol.

## Slide 27: Example: BGP flow control
OPEN
Initial database synchronization sends large volume of routes (UPDATEs) Often well above 1 million routes
UPDATE
BGP session comes up
Initial route table (RIB) database synchronization
BGP relies on TCP for flow-control (and reliability for that matter)

## Slide 28: Congestion control matters in the control plane
Control packets have strict priority over user packets
Large volume of control packets can still cause congestion
Congestive collapse of control protocols is not rare
  Flapping ISIS adjacencies self-reinforcing feedback loop
Solutions:
  Prioritize important control plane packets (mainly hellos)
  Multiple streams (QUIC, SCTP)
  Off-load liveness detection to separate protocol (BFD)

## Slide 29: Error control matters in the control plane
Control plane packets also get dropped
Need reliability mechanism (error control) in routing and signaling protocols
Approaches:
  Separate mechanism built-in to protocol itself: ISIS, OSPF, …
  Rely on transport (TCP) for reliability: BGP, LDP, …

## Slide 30: Example: ISIS error control
LSP 1
Partial Sequence Number PDU (PSNP) is used to ack LSP
There is also a Complete Sequence Number PDU (CSNP) that we don’t discuss here
PSNP acks LSP
LSP 2
PSNP 1 2
LSP 3
LSP 4
PSNP 4
LSP 3
PSNP 3
Time-out
LSP is transmitted if ack is not received

## Slide 31: Take-aways for quantum control protocols
You need to worry about flow control
You need to worry about congestion control
You need to worry about error control
Not just in the data plane, but also in the control plane
Avoid re-inventing the wheel: rely on layer 4 transport when possible This is somewhat contentious; it is my opinion that not everyone agrees with.

## Slide 32: Soft state versus hard state

## Slide 33: Soft state vs hard state
Soft state protocol
A.k.a. Periodic protocol
Sender initially sends data.
Receiver puts data in its database.
Sender periodically resends data (refresh).
If receiver doesn’t receive data anymore, it removes data from its database after time-out.
Heavy load due to periodic transmission.
Fallacy: simpler cleanup when sender crashes.
Sender wants to advertise some data (e.g. a route) to receiver.
Hard state state protocol
Runs protocol over reliable transport connection.
Sender initially sends data.
Receiver puts data in its database.
No periodic re-transmissions of data.
Receiver keep data in database until (a) sender explicitly withdraws data or (b) transport connection is disconnected.
No traffic if no changes in the database.
Needs reliable transport connection and keep-alive mechanism (typically TCP)

## Slide 34: Example: soft state in RSVP
PATH
PATH
PATH
RESV
RESV
RESV
PATH-refresh
PATH-refresh
PATH-refresh
RESV-refresh
RESV-refresh
RESV-refresh
PATH-refresh
PATH-refresh
PATH-refresh
RESV-refresh
RESV-refresh
RESV-refresh
Refresh interval
(~ 45 seconds)

## Slide 35: The problem with soft state
Typical network topology
Core router
Edge router Dual-homed to core router

## Slide 36: The problem with soft state
Typical network topology
Core router
Edge router Dual-homed to core router
Full mesh of LSPs From every edge router to every other edge router Traffic engineered according to bandwidth-demand matrix This diagram show logical topology of LSPs (not physical topology)

## Slide 37: The problem with soft state
Core router
Number of LSPs is O(N2)
When N is number of edge routers
Refresh frequency is O(N2)
Real-life example
Number of edge routers: 500
Number of LSPs: 500*499 = 249,500
Refresh interval = 45 seconds
Refresh traffic: 11,088 messages/sec (Simplifying assumption that all LSPs pass through the same core router)
This is not feasible in the control plane

## Slide 38: Example: hard state in BGP
UPDATE
UPDATE
UPDATE
KEEPALIVE
KEEPALIVE
KEEPALIVE
KEEPALIVE
KEEPALIVE
KEEPALIVE
UPDATE creates hard state
Can be > 1 million routes
Periodic refresh not feasible
Route stays valid until:
Explicitly WITHDRAW or
TCP connection breaks
Periodic KEEPALIVE
Needed to check TCP connection
Just a single message
Independent of number of routes

## Slide 39: Network meltdown due to Run-away replication

## Slide 40: Packet replication loops
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast)
Forwarding loop
Network meltdown
+
=

## Slide 41: Packet replication loops
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast)
Forwarding loop
No time to live (TTL) mechanism Packets can loop forever without ever being removed due to TTL expiry
Catastrophic network meltdown
+
+
=

## Slide 42: Ethernet address learning
11:11:11:11:11:11
22:22:22:22:22:22
33:33:33:33:33:33
Ethernet Address | Port
Switch layer 2 forwarding table
Port 1
Port 2
Port 3

## Slide 43: Ethernet address learning
11:11:11:11:11:11
22:22:22:22:22:22
33:33:33:33:33:33
Port 1
Port 3
Ethernet Address | Port
11:11:11:11:11:11 | 1
Switch layer 2 forwarding table
Unknown destination address: flood and learn source
Source Address | Destination Address | Payload
11:11:11:11:11:11 | 22:22:22:22:22:22 | …
Port 2

## Slide 44: Ethernet address learning
11:11:11:11:11:11
22:22:22:22:22:22
33:33:33:33:33:33
Port 1
Port 3
Ethernet Address | Port
11:11:11:11:11:11 22:22:22:22:22:22 | 1 2
Switch layer 2 forwarding table
Known destination address: unicast and learn source
Source Address | Destination Address | Payload
22:22:22:22:22:22 | 11:11:11:11:11:11 | …
Port 2

## Slide 45: Ethernet meltdown due to forwarding loop
Packet loop around the network at line rate
Number of packets grows exponentially

## Slide 46: Spanning Tree Protocol (STP)
STP removes loops by blocking links to form a spanning tree.
Wastes a lot of link capacity (no multipath)
Network melts down if STP doesn’t converge perfectly.

## Slide 47: Network meltdown due to Run-away state machine

## Slide 48: Typical 3-way adjacency finite state machine
State ONE-WAY
State TWO-WAY
State THREE-WAY
TX timer
TX HELLO(s=x)
TX timer
TX HELLO(s=x, n=y)
TX timer
TX HELLO(s=x, n=y)
RX HELLO(s=y)
-
RX HELLO(s=y, n=x)
-
RX HELLO(s=y, n=x)
-
RX HELLO(s=y, n=x)
-
X
Y
HELLO(s=x)
HELLO(s=x)
HELLO(s=x, n=y)
HELLO(s=x)
HELLO(s=y, n=x)
HELLO(s=y, n=x)
HELLO(s=y, n=x)
ONE-WAY
THREE-WAY
TWO-WAY
ONE
THREE-WAY
One HELLO message per timer interval (e.g. 10 seconds)
in each direction

## Slide 49: Run-away 3-way adjacency FSM
State NONE
State ONE-WAY
State TWO-WAY
TX timer
TX HELLO(s=x)
TX timer
TX HELLO(s=x, n=y)
TX timer
TX HELLO(s=x, n=y)
RX HELLO(s=y)
TX HELLO(s=x, n=y)
RX HELLO(s=y, n=x)
TX HELLO(s=x, n=y)
RX HELLO(s=y, n=x)
TX HELLO(s=x, n=y)
RX HELLO(s=y, n=x)
TX HELLO(s=x, n=y)
X
Y
HELLO(s=x)
HELLO(s=x, n=y)
HELLO(s=x, n=y)
HELLO(s=x, n=y)
HELLO(s=y, n=x)
HELLO(s=y, n=x)
HELLO(s=y, n=x)
NONE
THREE-WAY
ONE-
WAY
NONE
TWO-WAY
HELLO(s=y, n=x)
HELLO(s=x, n=y)
Non-stop line-rate of HELLOs
going back and forth

## Slide 50: Real life example: early draft of RIFT

## Slide 51: Network oscillation due to Run-away feedback loop

## Slide 52: Failed attempts at congestion-sensitive routing

## Slide 53: Take-aways for quantum control protocols
Make sure your protocols don’t have run-away scenarios
Beware of replication
Beware of amplifying feedback loops
Beware of oscillations

## Slide 54: Multi version Multi feature Multi vendor

## Slide 55: Interop between protocol versions
Version X needs to interoperate with version Y.
For any X and Y, not just Y = X + 1.
Don’t assume contiguous “regions” of same version.
Different devices will run different version of your protocol.
Temporarily during upgrade. You cannot upgrade your devices all at once; it takes a lot of time.
Or semi-permanently due to operational considerations (e.g. different vendors support different versions of the protocol). You want to be able to have multiple vendors in the same network.
Version 1
Version 2
Version 1
Version 1
Version 3

## Slide 56: Lessons learned from major version bumps
IPv4 vs IPv6
  IPv6 is not backwards compatible with IPv4
  Upgrading from IPv4 to IPv6 is a royal pain in the neck
  It’s been 20 years and IPv6 is still not universally deployed
  IPv4 will never go away
OSPFv3 vs OSPFv2
  OSPFv3 is not backwards compatible with OSPFv2
  You need to upgrade from OSPFv2 to OSPFv3 to get IPv6
  Real networks run OSPFv2 and OSPFv3
  ISIS did it right (ISIS with IPv6 can interoperate with ISIS without IPv6)
BGPv3 vs BGPv4 vs …BGPv5?
  BGPv3 is not backwards compatible with BGPv4, it required every Internet core router to be upgraded
  Upgrading every core router on the Internet is infeasible at this time
  BGPv4 has excellent extension mechanisms; it is unlikely that there will ever be a BGPv5

## Slide 57: Interop between feature sets
Protocol implementation that has feature A must interoperate with protocol implementation that does not have feature A.
Different vendors and versions of code have different feature sets.
Don’t assume the feature set can be derived from the protocol version. Allows protocol extensions to evolve and be deployed independently.
Don’t assume the feature set is the same. Feature set A+B must interoperate with B+C.
A
B
C
D
Protocol features
A
A
A
B
B
B
C
C
C
D
D
D

## Slide 58: Capability announcement (“negotiation”)
I support features B, C, D
We can use features B, C (these are the ones we have in common)
A
B
C
B
C
D
I support features A, C, D
We can use features B, C (these are the ones we have in common)
(Things get a bit more complicated when more than 2 devices are involved, e.g. flooding)

## Slide 59: Example: BGPv4 capabilities

## Slide 60: Type Length Value (TLV) Encoding

## Slide 61: How to handle unrecognized TLVs?
What should you do when you receive a TLV with an unknown type?
Happens when another device is running a newer version of the protocol.
Options:
  Ignore and propagate the TLV
  Ignore and remove the TLV
  Declare an error
  Note: ignoring is possible because the length L is known and the value can be skipped
The originator of the TLV (who by definition understands it) sets some extra bits in the TLV to instruct the receiver what to do.

## Slide 62: Example: Label Distribution Protocol (LDP)
TLV encoding is also used in:
BGP
OSPF
ISIS
RSVP
Many more…

## Slide 63: Control protocol security

## Slide 64: Authentication vs encryption

## Slide 65: Neighbor authentication

## Slide 66: Origin authentication

## Slide 67: Path authentication

## Slide 68: Planned upgrades Unplanned crashes

## Slide 69: Chassis devices
Everything (routing engine, switch fabric, power supplies, fans, …) redundant and in-service replaceable
Redundant control planes (routing engines)

## Slide 70: In-Service Software Upgrade (ISSU)
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 1
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 2
Standby routing engine:
Version 2
Upgrade
standby
Switch-over
Upgrade
new standby

## Slide 71: Non-Stop Forwarding (NSF) Also known as Graceful Restart (GR)
Forwarding engine STALE TABLES
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESYNCHRONIZE
Control-plane session RESYNCHRONIZE
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESTART FINISHED
Control-plane session RESTART FINISHED
Data-plane traffic
Data-plane traffic
Control-plane session
PREPARE FOR RESTART
Control-plane session PREPARE FOR RESTART

## Slide 72: Pizza-box devices
Does not have redundant routing hardware routing engines.
(Sometimes in redundant software routing engines using virtual machines or containers.)

## Slide 73: Non-Stop Routing (NSR)

## Slide 74: Scale-out instead of scale-up

## Slide 75: Relatively small impact of losing one device
For planned upgrades, announce in advance (e.g. overload flag) to shift traffic away, if possible.

## Slide 76: Don’t hand-code your parsers
Type Length Value (TLV) encoding (we saw this before!)
Formal modeling language for on-the-wire protocol
  Abstract Syntax Number 1 (ASN.1)
  YANG
  Google Protocol Buffers (BGP), Thrift, etc.
@@@ Example of real-life bug

## Slide 77: References
Some lessons from history (“Those who do not know history are doomed to repeat it”) https://datatracker.ietf.org/meeting/102/materials/slides-102-rtgarea-those-who-do-not-learn-history-are-doomed-to-repeat-it-00

## Slide 78: Thank you.