## Slide 1: Protocol Design Considerations
Version 1, Presented at QuTech (Delft) on 22 November 2019

## Slide 2: A few true stories…

## Slide 3: Designing correct protocols is hard
On 27 October 1980, all routers in the entire Internet had to be rebooted simultaneously to recover from a protocol design weakness.
http://www.hannaypublications.com/portfolio/wp-content/uploads/2016/02/AppliedComms_A2.pdf

## Slide 4: Version numbers to pick newest message
Message
Version number 8
Message
Version number 40
Message
Version number 44
<
<
Note: this mechanism is still used today, for example in OSPF and ISIS link state flooding
Oldest version
Newest version

## Slide 5: Modulo 64 comparison creates ”loop”
Version field was unsigned 6 bit integer, so math is modulo 64
Competing message versions kept replacing each other forever, eating up all CPU
The versions were introduced to a double bit error, which was not detected because check-sums were disabled.
Z
Message
Version number 8
Message
Version number 40
Message
Version number 44
8 < 40
(modulo 64)
40 < 44
(modulo 64)
44 < 8
(modulo 64)

## Slide 6: Still making the same mistakes today
A similar problem exists in the BGP specification and is observed in the Internet to this day.
See BGP persistent route oscillations (RFC3345)

## Slide 7: Implementing protocols correctly is hard
A bug in a widely used BGP implementation allowed an attacker to advertise a BGP route that caused many BGP routers on the other side of the world to crash.
Sending a specially constructed 4-octet AS-path caused certain routers to crash CVE-2014-3818 https://securitytracker.com/id/1031009

## Slide 8: Protocol security is hard
A BGP vulnerability enabled hackers to rob a bitcoin bank.
https://www.wired.com/2014/08/isp-bitcoin-theft/

## Slide 9: Flow control Congestion control Error control (reliability) in the data plane

## Slide 10: Flow control
Make sure sender does not produce data faster
than receiver can consume them.
Note: here it is the receiver that is not keeping up; the network can keep up fine.
Send 5 packets per second (pps)
Consume 3 pps
Drop 2 pps
Receive buffer overflows.
Buffer can absorb bursts but not sustained rate difference.

## Slide 11: Flow control in quantum network
Qubit to be teleported
Sender never stores more than one “qubit to be sent” in memory
Qubit that has been teleported
Receiver needs to store it in memory until it is consumed (measured)
Make sure sender does not produce qubits faster
than receiver can consume them.
Bell pair
Ideally, it is produced “fresh” just before we have a qubit to teleport
Consumer can run out of qubit memory ifs sender sends too fast

## Slide 12: Flow control approaches
General principle: make the data arrive more slowly
Approach 1: Sliding window
  It is okay to receive data later (delay in-sensitive traffic)
  Web pages, file transfer, e-mail, …
  Receiver makes the sender slow down
Approach 2: Adaptive encoding
  It is not okay to receive data later (delay-sensitive traffic)
  Voice, live video, video on demand, …
  Receiver makes the send send less data
Sender must be able to back-pressure application

## Slide 13: Sliding window
Window size = 5
Window size = 3
Window size = 2
Window size = 0
Consumed

## Slide 14: Bandwidth-delay product
100 Gbps, 5000 km (= 50 ms round-trip @ speed of light in fiber)
In this example window size (= receive buffer size) is 100 MB = 800 Mbit
Only 32% of available bandwidth is used.
Window size must be ≥ bandwidth * round-trip delay to fully utilize available capacity.
window size 800 Mbit @
100 Gbps = 8 ms
Round-trip time 25 ms

## Slide 15: Congestion control
Make sure senders do not produce data faster
than network can carry it.
Send link-rate
Send link-rate
Try to send 2x link-rate traffic on link.
Transmit buffer overflows.
Drop half of traffic.

## Slide 16: Congestion control in quantum networks
End-points cannot get more end-to-end Bell pairs per second (Bpps) than network can produce them
based on bottleneck link or router.
10 Bpps
10 Bpps

## Slide 17: Congestion control
Mechanisms to avoid congestion
General principle: send traffic more slowly when congestion occurs
Detect dropped packets at transport layer and reduce window
  TCP slow start algorithm
  Extremely difficult to ”get right” (TCP Reno, Vegas, high speed, BIC, CUBIC, C2TCP, NATCP, Elastic TCP, and many many more variations)
  Assumes everyone “plays fair”
Backwards Explicit Congestion Notification (BECN)
  @@@
Forward Explicit Congestion Notification (FECN)
  Set bits in forwarded IP packet: Congestion Encountered (CE)
  Requires cooperation from the transport layer to slow down

## Slide 18: Active Queue Management (AQM)
Mechanism for dealing with congestion when it does occur
Decide which packet to service next in the send queue
  Classification: @@@
  Hierarchical schedulers: @@@
  Shapers: @@@
Decide when to start dropping packets
  Tail-drop
  Random Early Drop (RED)
Decide which packet to drop
  In-profile vs out-of-profile

## Slide 19: Hierarchical queue scheduler
Source https://www.juniper.net/documentation/en_US/junos/information-products/pathway-pages/cos/config-guide-hierarchical-cos.pdf

## Slide 20: Reliable transport @@@
Error detection and recovery
1
2
3
4
5
6
7
12
8
9
10
11

## Slide 21: Error detection mechanisms
@@@

## Slide 22: Error recovery mechanisms mechanisms
@@@

## Slide 23: Reliable transport (error control)
@@@ Picture

## Slide 24: Reliable transport approaches
@@@ ACK
@@@ NACK
@@@ Selective ACK

## Slide 25: Mixing up flow, congestion and error control
@@@ bad idea @@@
@@@ sender cannot distinguish
  slow receiver
@@@ re-ordering packets is disastrous

## Slide 26: Soft state versus Hard state

## Slide 27: Soft state vs hard state
Soft state protocol
A.k.a. Periodic protocol
Sender initially sends data.
Receiver puts data in its database.
Sender periodically resends data.
If receiver doesn’t receive data anymore, it removes data from its database after time-out.
Heavy load due to periodic transmission.
Fallacy: simpler cleanup when sender crashes.
Sender wants to advertise some data (e.g. a route) to receiver.
Hard state state protocol
Runs protocol over reliable transport connection.
Sender initially sends data.
Receiver puts data in its database.
No periodic re-transmissions of data.
Receiver keep data in database until (a) sender explicitly withdraws data or (b) transport connection is disconnected.
No traffic if no changes in the database.
Needs reliable transport connection and keep-alive mechanism.

## Slide 28: Flow control Congestion control Error control (reliability) in the control plane

## Slide 29: Explosions and oscillations in your network

## Slide 30: Packet replication loops
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast) +
Forwarding loop
=
Network meltdown
Due to explosion of traffic

## Slide 31: Packet replication loops
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast) +
Forwarding loop
+
Absence of TTL mechanism
Packets can loop forever without TTL expiring
=
Disastrous nearly unfixable network meltdown
Due to explosion of traffic which doesn’t go away, even after you shut up the source

## Slide 32: Example: Ethernet address learning + SPT
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast) +
Forwarding loop
=
Network meltdown
Due to explosion of traffic

## Slide 33: Triggered state machine loops

## Slide 34: Run-away replication
Ethernet example

## Slide 35: Undampened control feedback loops
Failed attempts at delay routing

## Slide 36: Undampened state machine feedback loops
RIFT example

## Slide 37: Multi version Multi feature Multi vendor

## Slide 38: Interop between protocol versions
Version X needs to interoperate with version Y.
For any X and Y, not just Y = X + 1.
Don’t assume contiguous “regions” of same version.
Different devices will run different version of your protocol.
Temporarily during upgrade. You cannot upgrade your devices all at once; it takes a lot of time.
Or semi-permanently due to operational considerations (e.g. different vendors support different versions of the protocol). You want to be able to have multiple vendors in the same network.
Version 1
Version 2
Version 1
Version 1
Version 3

## Slide 39: Lessons learned from major version bumps
IPv4 vs IPv6
  IPv6 is not backwards compatible with IPv4
  Upgrading from IPv4 to IPv6 is a royal pain in the neck
  It’s been 20 years and IPv6 is still not universally deployed
  IPv4 will never go away
OSPFv3 vs OSPFv2
  OSPFv3 is not backwards compatible with OSPFv2
  You need to upgrade from OSPFv2 to OSPFv3 to get IPv6
  Real networks run OSPFv2 and OSPFv3
  ISIS did it right (ISIS with IPv6 can interoperate with ISIS without IPv6)
BGPv3 vs BGPv4 vs …BGPv5?
  BGPv3 is not backwards compatible with BGPv4, it required every Internet core router to be upgraded
  Upgrading every core router on the Internet is infeasible at this time
  BGPv4 has excellent extension mechanisms; it is unlikely that there will ever be a BGPv5

## Slide 40: Interop between feature sets
Protocol implementation that has feature A must interoperate with protocol implementation that does not have feature A.
Different vendors and versions of code have different feature sets.
Don’t assume the feature set can be derived from the protocol version. Allows protocol extensions to evolve and be deployed independently.
Don’t assume the feature set is the same. Feature set A+B must interoperate with B+C.
A
B
C
D
Protocol features
A
A
A
B
B
B
C
C
C
D
D
D

## Slide 41: Capability announcement (“negotiation”)
I support features B, C, D
We can use features B, C (these are the ones we have in common)
A
B
C
B
C
D
I support features A, C, D
We can use features B, C (these are the ones we have in common)
(Things get a bit more complicated when more than 2 devices are involved, e.g. flooding)

## Slide 42: Example: BGPv4 capabilities

## Slide 43: Type Length Value (TLV) Encoding

## Slide 44: How to handle unrecognized TLVs?
What should you do when you receive a TLV with an unknown type?
Happens when another device is running a newer version of the protocol.
Options:
  Ignore and propagate the TLV
  Ignore and remove the TLV
  Declare an error
  Note: ignoring is possible because the length L is known and the value can be skipped
The originator of the TLV (who by definition understands it) sets some extra bits in the TLV to instruct the receiver what to do.

## Slide 45: Example: Label Distribution Protocol (LDP)
TLV encoding is also used in:
BGP
OSPF
ISIS
RSVP
Many more…

## Slide 46: Planned upgrades Unplanned crashes

## Slide 47: Authentication vs encryption

## Slide 48: Neighbor authentication

## Slide 49: Origin authentication

## Slide 50: Path authentication

## Slide 51: Control protocol security

## Slide 52: Chassis devices
Everything (routing engine, switch fabric, power supplies, fans, …) redundant and in-service replaceable
Redundant control planes (routing engines)

## Slide 53: In-Service Software Upgrade (ISSU)
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 1
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 2
Standby routing engine:
Version 2
Upgrade
standby
Switch-over
Upgrade
new standby

## Slide 54: Non-Stop Forwarding (NSF) Also known as Graceful Restart (GR)
Forwarding engine STALE TABLES
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESYNCHRONIZE
Control-plane session RESYNCHRONIZE
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESTART FINISHED
Control-plane session RESTART FINISHED
Data-plane traffic
Data-plane traffic
Control-plane session
PREPARE FOR RESTART
Control-plane session PREPARE FOR RESTART

## Slide 55: Pizza-box devices
Does not have redundant routing hardware routing engines.
(Sometimes in redundant software routing engines using virtual machines or containers.)

## Slide 56: Non-Stop Routing (NSR)

## Slide 57: Scale-out instead of scale-up

## Slide 58: Relatively small impact of losing one device
For planned upgrades, announce in advance (e.g. overload flag) to shift traffic away, if possible.

## Slide 59: Implementation correctness is hard. Much harder than you think.

## Slide 60: Don’t hand-code your parsers
Type Length Value (TLV) encoding (we saw this before!)
Formal modeling language for on-the-wire protocol
  Abstract Syntax Number 1 (ASN.1)
  YANG
  Google Protocol Buffers (BGP), Thrift, etc.
@@@ Example of real-life bug

## Slide 61: Thank you.

## Slide 62: References
Some lessons from history (“Those who do not know history are doomed to repeat it”) https://datatracker.ietf.org/meeting/102/materials/slides-102-rtgarea-those-who-do-not-learn-history-are-doomed-to-repeat-it-00