## Slide 1: Protocol Design Considerations
Bruno Rijsman
Version 1, Presented at QuTech (Delft) on 22 November 2019

## Slide 2: A few true stories…

## Slide 3: Designing correct protocols is hard
On 27 October 1980, all routers in the entire Internet had to be rebooted simultaneously to recover from a protocol design weakness.
http://www.hannaypublications.com/portfolio/wp-content/uploads/2016/02/AppliedComms_A2.pdf

## Slide 4: Version numbers to pick newest message
Message
Version number 8
Message
Version number 40
Message
Version number 44
<
<
Note: this mechanism is still used today, for example in OSPF and ISIS link state flooding
Oldest version
Newest version

## Slide 5: Modulo 64 comparison creates ”version loop”
Version field was unsigned 6-bit integer, so math is modulo 64
Competing message versions kept replacing each other forever, eating up all CPU
The versions were introduced to a double bit error, which was not detected because check-sums were disabled.
Message
Version number 8
Message
Version number 40
Message
Version number 44
8 < 40
(modulo 64)
40 < 44
(modulo 64)
44 < 8
(modulo 64)

## Slide 6: We have not quite yet learned our lessons
A similar problem exists in the BGP specification and is observed in the Internet to this day.
See BGP persistent route oscillations (RFC3345)

## Slide 7: Implementing protocols correctly is hard
A bug in a widely used BGP implementation allowed an attacker to advertise a BGP route that caused many BGP routers on the other side of the world to crash.
Sending a specially constructed 4-octet AS-path caused certain routers to crash CVE-2014-3818 https://securitytracker.com/id/1031009

## Slide 8: Protocol security is hard
A BGP vulnerability enabled hackers to rob a bitcoin bank.
https://www.wired.com/2014/08/isp-bitcoin-theft/

## Slide 9: Planning for evolution Multi-version, multi-feature, multi-vendor networks

## Slide 10: Your protocol will evolve over time
Typical versioning scheme:
  Minor version bump = backwards compatible
  Major version bump = not backwards compatible
  In practice, this does not work!
Examples of doing it wrong:
  IPv4 to IPv6
  OSPFv2 to OSPFv3
Examples of doing it right
  ISIS
  BGP
  Evolve features without breaking backwards compatibility
If you don’t design your protocol with the future in mind, every new feature will be a major version bump…

## Slide 11: The problem with major version bumps
It’s extremely hard avoiding running different major versions in your network if major bumps happen frequently.
Temporarily during upgrade. You cannot upgrade your devices all at once; it takes a lot of time.
Or semi-permanently due to operational considerations (e.g. different vendors support different versions of the protocol). You want to be able to have multiple vendors in the same network.
Your network will be partitioned. Having a partitioned network makes finishing the upgrade nearly impossible.
Version 1.0
Version 2.0
Version 1.0
Version 1.1
Version 3.0
Partitions

## Slide 12: A better approach based on features
Protocol implementation that has feature A must interoperate with protocol implementation that does not have feature A.
Different vendors and versions of code have different feature sets.
Don’t assume the feature set can be derived from the protocol version. Allows protocol extensions to evolve and be deployed independently.
Don’t assume the feature set is the same. Feature set A+B must interoperate with B+C.
A
B
C
D
Protocol features (aka capabilities)
A
A
A
B
B
B
C
C
C
D
D
D

## Slide 13: Capability announcement (“negotiation”)
I support features B, C, D
We can use features B, C (these are the ones we have in common)
A
B
C
B
C
D
I support features A, C, D
We can use features B, C (these are the ones we have in common)
(Things get a bit more complicated when more than 2 devices are involved, e.g. flooding)

## Slide 14: Example: BGPv4 capabilities

## Slide 15: Type Length Value (TLV) Encoding
Makes it easy for old versions of the protocol to interoperate with new versions of the protocol.
Also avoid bugs in the code by making it easier to write parsers.
Used in almost all modern protocols (OSPF, ISIS, BGP, RSVP, …)

## Slide 16: Type Length Value (TLV) Encoding
Type code
Length
Value
What does it mean?
How many bytes?
Very easy to parse; less chance of bugs in parses.

## Slide 17: Hierarchical TLVs
Type
Length
Value
Type
Length
Value
Type
Length
Value
Sub-Type
Length
Value
Sub-Type
Length
Value
TLVs
Sub-TLVs
Sub-Sub-Type
Length
Value
Sub-Sub-Type
Length
Value
Sub-Sub-TLVs

## Slide 18: Easy to skip unknown TLVs
Type
Length
Value
Type
Length
Value
Type
Length
Value
Known types
Can parse and act on values
Unknown type (unknown feature, future version of protocol, ..)
Enables receiver to skip and ignore the unknown value
(but is that the right thing to do?)
Don’t know how to parse this or act on it

## Slide 19: Example: IANA ISIS TLV code point registry

## Slide 20: How to handle unrecognized TLVs?
What should you do when you receive a TLV with an unknown type?
Happens when another device is running a newer version of the protocol.
Options:
  Ignore and propagate the TLV
  Ignore and remove the TLV
  Declare an error
  Note: ignoring is possible because the length L is known and the value can be skipped
The originator of the TLV (who by definition understands it) sets some extra bits in the TLV to instruct the receiver what to do.

## Slide 21: Example: Label Distribution Protocol (LDP)
TLV encoding is also used in:
BGP
OSPF
ISIS
RSVP
Many more…

## Slide 22: Beyond TLVs: formal modeling languages
Encoded message on the wire
BER, CER, NETCONF, RESTCONF, GPB
Protocol message data model
Abstract syntax: ASN1, YANG, GPB
Generated code for
encoding and decoding messages Local syntax: Rust objects
Protocol implementation
Modeling language compiler
Generated code for
encoding and decoding messages
Local syntax: Python objects
Protocol implementation

## Slide 23: Examples
Modeling language | Protocols
ASN.1 | Simple Network Management Protocol (SNMP)
ASN.1 | Light-weight Directory Access Protocol (LDAP)
YANG | Network Configuration Protocol (NETCONF)
Protobuf | GRPC Network Management Interface (gNMI)
Thrift | Routing In Fat Trees (RIFT)

## Slide 24: Examples
ASN.1 model for LDAP protocol
YANG model for interface management
Thrift model for RIFT protocol

## Slide 25: Control protocol security

## Slide 26: Control plane security
Authentication
  Is the router that I am talking to really the router it claims to be?
Integrity
  Are the routing messages modified or spoofed by an adversary?
  Special case: replay attack
Confidentiality?
  Encrypt the protocol messages (often not a requirement)
Authorization
  Is this router allowed to have an adjacency with me?
  Is this router allowed to advertise this route?
    If it originates the route, can it prove it owns the prefix?
    If it propagated the route, can it prove that the advertised path is correct?

## Slide 27: Neighbor authentication and integrity
Pre-shared key configured on each router
Sign each message with secure hash using pre-shared key
Add sequence number to prevent replay attacks
Message often not encrypted
Protocol
Message
Sequence nr
Signature
Pre-shared key
Sender increases
Receiver checks increasing
Secure hash function

## Slide 28: Link state flooding: origin and outer key
A
B
C
Link State
Flooded by A
Origin Signature
Signed by A
Sequence Nr
Added by A
Outer Signature
Signed by A
Link State
Flooded by A
Origin Signature
Signed by A
Sequence Nr
Added by B
Outer Signature
Signed by B
D
Link State
Flooded by A
Origin Signature
Signed by A
Sequence Nr
Added by C
Outer Signature
Signed by C
Every router in the networks must have the same pre-shared origin key (not feasible for IDR)
Pre-shared outer keys can be different per link, but are the same in practice
Pre-shared key roll-over is very painful; often does not happen in practice

## Slide 29: BGP prefix hijacking
Internet Registry (IR)
Assign:
AS 103
Address 1.1.1.0/24
BGP UPDATE
Prefix: 1.1.1.0/24
AS-Path: 103
AS 101
AS 102
AS 100
AS 104
AS 103
BGP UPDATE
Prefix: 1.1.1.0/24
AS-Path: 102 103
BGP UPDATE
Prefix: 1.1.1.0/24
AS-Path: 101 102 103

## Slide 30: BGP prefix hijacking
Internet Registry (IR)
Assign:
AS 103
Address 1.1.1.0/24
BGP UPDATE
Prefix: 1.1.1.0/24
AS-Path: 103
AS 101
AS 102
AS 100
AS 104
AS 103
BGP UPDATE
Prefix: 1.1.1.0/24
AS-Path: 102 103
BGP UPDATE
Prefix: 1.1.1.0/24
AS-Path: 101 102 103
BGP UPDATE
Prefix: 1.1.1.0/24
AS-Path: 104
Accidental or malicious invalid BGP UPDATE
AS 104 does not own prefix 1.1.1.0/24

## Slide 31: BGP route origin authentication (ROA) (Simplified)
Autonomous System 701
Autonomous System 2686
Autonomous System 286
Internet Registry (IR)
Assign:
AS number: 701
Address block: 100.1.0.0/16
Public Repository
Validator
aka validating cache
Validator
ROA
AS 701
Block 100.1.0.0/16
Signed by IR
Validate signature
and cache ROA
Check each received
UPDATE
BGP UPDATE
Prefix: 100.1.0.0/16
AS-Path: 701
BGP UPDATE
Prefix: 100.1.0.0/16
AS-Path: 2686 701

## Slide 32: Also need BGP path validation
Provider X
Provider Y
Customer A
Customer B
Customer C
A
A
Accidental violation of valley-fee routing
Y should not do transit through customer B
B should not advertise A to Y
Y should not accept A from B
(There are also malicious flavors of this, e.g. BGP poisoning)

## Slide 33: Upgrades, crashes There is no maintenance window for the Internet

## Slide 34: Chassis devices
Everything (routing engine, switch fabric, power supplies, fans, …) redundant and in-service replaceable
Redundant control planes (routing engines)

## Slide 35: In-Service Software Upgrade (ISSU)
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 1
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 1
Standby routing engine:
Version 2
Forwarding engine
Forwarding engine
Active routing engine
Version 2
Standby routing engine:
Version 2
Upgrade
standby
Switch-over
Upgrade
new standby

## Slide 36: Non-Stop Forwarding (NSF) Also known as Graceful Restart (GR)
Forwarding engine STALE TABLES
Active routing engine: version 1
Standby routing engine: version 2
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
RESYNCHRONIZE
Control-plane session RESYNCHRONIZE
Data-plane traffic
Data-plane traffic
Control-plane session
PREPARE FOR RESTART
Control-plane session PREPARE FOR RESTART
temporarily
NO control plane session
temporarily
NO control plane session

## Slide 37: Non-Stop Routing (NSR)
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Data-plane traffic
Data-plane traffic
Forwarding engine
Active routing engine: version 1
Standby routing engine: version 2
Control-plane session
Control-plane session
Data-plane traffic
Data-plane traffic
Control-plane session
Control-plane session
Switchover a LIVE control plane session (TCP connection)
Incredibly difficult; requires constant synchronization of TCP state
Cause more problems than it solves in real life.
Modern approach: use scale-out instead of scale-up (when possible)

## Slide 38: Pizza-box devices
Does not have redundant routing hardware routing engines.
(Sometimes in redundant software routing engines using virtual machines or containers.)
Cheap commodity hardware

## Slide 39: Scale-out instead of scale-up
Scale-up
One large chassis switch
Internal switch fabric
If switch fails, all is lost
NSF or NSR for upgrade
Everything must be redundant
Expensive
Complex
Scale-out
Multiple small pizza-box switches
Clos fabric
If one switch fails, only 1/Nth of capacity lost
Rolling upgrade
No redundancy needed inside switch
Cheap
Simple

## Slide 40: Flow control Congestion control Error control in the data plane

## Slide 41: Flow control
Make sure the sender does not produce data faster
than the receiver can consume it.
Note: here it is the receiver that is not keeping up; the network can keep up fine.
Send 5 packets per second (pps)
Consume 3 pps
Drop 2 pps
Receive buffer overflows.
Buffer can absorb bursts but not sustained rate difference.

## Slide 42: Flow control in quantum network
Qubit to be teleported
Sender never stores more than one “qubit to be sent” in memory
Qubit that has been teleported
Receiver needs to store it in memory until it is consumed (measured)
Make sure sender does not produce qubits faster
than receiver can consume them.
Bell pair
Ideally, it is produced “fresh” just before we have a qubit to teleport
Consumer can run out of qubit memory ifs sender sends qubits
faster than received consumes (measures) them.
[Animation]

## Slide 43: Flow control approaches
General principle: make the data arrive more slowly
Approach 1: Sliding window
  Receiver makes the sender slow down by delaying permission to send
  It is okay to receive data later (delay in-sensitive traffic)
  Web pages, file transfer, e-mail, …
Approach 2: Adaptive encoding
  The sender sends less data by switching to more lossy compression
  It is not okay to receive data later (delay-sensitive traffic)
  Voice, live video, video on demand, …
Related approach: Time slot scheduling
  Used in Time Division Multiplexing (TDM) and wireless networks
  Avoids congestion from happening in the first place
Sender must be able to back-pressure application

## Slide 44: Sliding window
Window size = 5
Window size = 3
Window size = 2
Window size = 0
Consumed
Buffer size 5

## Slide 45: Bandwidth-delay product
100 Gbps, 5000 km (= 50 ms round-trip @ speed of light in fiber)
Window size must be ≥ bandwidth * round-trip delay to fully utilize available bandwidth.
In this example window size (= receive buffer size) is 100 MB = 800 Mbit
Only 32% of available bandwidth is used.
window size 800 Mbit @
100 Gbps = 8 ms
Round-trip time 25 ms

## Slide 46: Congestion
Make sure senders do not produce data faster
than network can carry it.
Send link-rate
Send link-rate
Try to send 2x link-rate traffic on link.
Transmit buffer overflows.
Drop half of traffic.

## Slide 47: Congestion control
Congestion avoidance: avoid congestion in the first place
Congestion mitigation: deal with congestion when it does occur
Worst case scenario: congestive collapse
  Effective capacity of the network to carry useful traffic drops to zero
  Retransmissions due to excessive drops and queueing delays overwhelm network
  More likely to happen when capacity is low compared to demand (as it will be in early quantum networks!)
  This actually happened in the early internet: in 1986 the capacity collapsed from 32 Kbps to 40 bps (not Kbps) https://blog.acolyer.org/2015/05/21/congestion-avoidance-and-control/ https://tools.ietf.org/html/rfc896

## Slide 48: Congestion avoidance
Congestion avoidance: mechanisms to avoid congestion in the first place
General principle: send traffic more slowly when congestion occurs
TCP congestion control
  TCP tries to estimate maximum rate before congestion occurs
  TCP sender dynamically congestion window based on presence or absence of drops
  Extremely difficult to get right: Reno, Vegas, BIC, CUBIC, …. and many more algorithms
  Assumes everyone plays fair
Backwards Explicit Congestion Notification (BECN)
  Router sends message to source to slow down when it observes congestion
Forward Explicit Congestion Notification (FECN)
  Set bits in forwarded IP packet: Congestion Encountered (CE)
  Requires cooperation from the transport layer to slow down

## Slide 49: Congestion mitigation
Active Queue Management (AQM):
  Mechanism for dealing with congestion when it does occur
  Queueing only happens if there is contention = congestion
Decide which packets are most important
  Classification at the edge
  Mark classification result into QoS / precedence bits in packet header
Decide which packet to service next in the send queue
  Hierarchical schedulers
  Shapers
Decide when to start dropping packets and which packet to drop
  Tail-drop
  Random Early Drop (RED)
  Drop out-of-profile packet before in-profile packets

## Slide 50: Hierarchical queue scheduler
Source https://www.juniper.net/documentation/en_US/junos/information-products/pathway-pages/cos/config-guide-hierarchical-cos.pdf

## Slide 51: “Congestion control” in quantum networks
End-points cannot get more end-to-end Bell pairs per second (Bpps) than network can produce them
based on bottleneck link or router.
10 Bpps
10 Bpps
10 Bpps
10 Bpps
10 Bpps
Desire X Bpps
Desire Y Bpps
Bottleneck link.
Cannot achieve desired end-to-end entanglements if X+Y > 10
(or even less considering non-deterministic swaps and distillation)

## Slide 52: Reliable transport: error detection and recovery
This is an example of the go-back-N error recovery
1
2
3
4
Time-out
waiting for akc-2
based on estimate RTT
Retransmit packets +
Adjust congestion window
2
3
Retransmit
Retransmit
4
Retransmit
Ack 1
Ack 2
Ack 3
Dropped
(most likely due to congestion)

## Slide 53: Error detection and recovery mechanisms
Checksums
  To detect transmission errors
  Classical networks are so reliable that the vast majority of drops are due to congestion
Automatic Repeat Request (ARQ)
  Receiver sends an acknowledgement (ack) when it has correctly received the data
  The sender re-transmits the data when it does not receive the ack
  Not an option for quantum networks (requires that the sender keeps a copy until the data is acknowledged, in case the data needs to be retransmitted).
  Go-back-N: resend all data starting at the dropped packet
  Selective repeat: only resend the data that was dropped (requires selective ack)
Forward Error Correction (FEC)
  When error rate is too high (noisy links)
  When retransmission is delay is not acceptable (e.g. long latency satellite links)
  The only option in quantum networks (quantum error correcting codes)

## Slide 54: What is so difficult about this?
Flow control, congestion control, and error control are separate but closely related concepts
Most transport protocols don’t have clean separation of concerns
For example, in TCP absence of ACK can mean many things:
  Flow control: receiver wants us to slow down
  Error: data packet or ACK was dropped
  Congestion: data packet or ACK was delayed in queue
Over time TCP has been enhanced:
  Selective acknowledgement (SACK)
  Timestamps

## Slide 55: Flow control Congestion control Error control in the control plane

## Slide 56: Flow control matters in the control plane
Routing and signaling protocols exchange large volumes of data
Sender must not overwhelm receiver
Flow control approaches in routing and signaling protocols:
  Fixed pacing
  Flow control mechanism built into the protocol itself
  Rely on TCP flow control

## Slide 57: Example: ISIS flow control
IIH
Initial database synchronization sends large volume of link state packets (LSPs) Potentially tens of thousands of LSPs
LSP
ISIS adjacency comes up
Initial link-state database (LSDB) synchronization
Pacing parameters in standard, e.g. minimumLSPTransmissionInterval
Recent proposals to dynamically control intervals in ISIS protocol.

## Slide 58: Example: BGP flow control
OPEN
Initial database synchronization sends large volume of routes (UPDATEs) Often well above 1 million routes
UPDATE
BGP session comes up
Initial route table (RIB) database synchronization
BGP relies on TCP for flow-control (and reliability for that matter)

## Slide 59: Congestion control matters in the control plane
Control packets have strict priority over user packets
Large volume of control packets can still cause congestion
Congestive collapse of control protocols is not rare
  Flapping ISIS adjacencies self-reinforcing feedback loop
Solutions:
  Prioritize important control plane packets (mainly hellos)
  Multiple streams (QUIC, SCTP)
  Off-load liveness detection to separate protocol (BFD)

## Slide 60: Error control matters in the control plane
Control plane packets also get dropped
Need reliability mechanism (error control) in routing and signaling protocols
Approaches:
  Separate mechanism built-in to protocol itself: ISIS, OSPF, …
  Rely on transport (TCP) for reliability: BGP, LDP, …

## Slide 61: Example: ISIS error control
LSP 1
Partial Sequence Number PDU (PSNP) is used to ack LSP
There is also a Complete Sequence Number PDU (CSNP) that we don’t discuss here
PSNP acks LSP
LSP 2
PSNP 1 2
LSP 3
LSP 4
PSNP 4
LSP 3
PSNP 3
Time-out
LSP is transmitted if ack is not received

## Slide 62: Take-aways for quantum control protocols
You need to worry about flow control
You need to worry about congestion control
You need to worry about error control
Not just in the data plane, but also in the control plane
Avoid re-inventing the wheel: rely on layer 4 transport when possible This is somewhat contentious; it is my opinion that not everyone agrees with.

## Slide 63: Soft state versus hard state

## Slide 64: Soft state vs hard state
Soft state protocol
A.k.a. Periodic protocol
Sender initially sends data.
Receiver puts data in its database.
Sender periodically resends data (refresh).
If receiver doesn’t receive data anymore, it removes data from its database after time-out.
Heavy load due to periodic transmission.
Fallacy: simpler cleanup when sender crashes.
Sender wants to advertise some data (e.g. a route) to receiver.
Hard state state protocol
Runs protocol over reliable transport connection.
Sender initially sends data.
Receiver puts data in its database.
No periodic re-transmissions of data.
Receiver keep data in database until (a) sender explicitly withdraws data or (b) transport connection is disconnected.
No traffic if no changes in the database.
Needs reliable transport connection and keep-alive mechanism (typically TCP)

## Slide 65: Example: soft state in RSVP
PATH
PATH
PATH
RESV
RESV
RESV
PATH-refresh
PATH-refresh
PATH-refresh
RESV-refresh
RESV-refresh
RESV-refresh
PATH-refresh
PATH-refresh
PATH-refresh
RESV-refresh
RESV-refresh
RESV-refresh
Refresh interval
(~ 45 seconds)

## Slide 66: The problem with soft state
Typical network topology
Core router
Edge router Dual-homed to core router

## Slide 67: The problem with soft state
Typical network topology
Core router
Edge router Dual-homed to core router
Full mesh of LSPs From every edge router to every other edge router Traffic engineered according to bandwidth-demand matrix This diagram show logical topology of LSPs (not physical topology)

## Slide 68: The problem with soft state
Core router
Number of LSPs is O(N2)
When N is number of edge routers
Refresh frequency is O(N2)
Real-life example
Number of edge routers: 500
Number of LSPs: 500*499 = 249,500
Refresh interval = 45 seconds
Refresh traffic: 11,088 messages/sec (Simplifying assumption that all LSPs pass through the same core router)
This is not feasible in the control plane

## Slide 69: Example: hard state in BGP
UPDATE
UPDATE
UPDATE
KEEPALIVE
KEEPALIVE
KEEPALIVE
KEEPALIVE
KEEPALIVE
KEEPALIVE
UPDATE creates hard state
Can be > 1 million routes
Periodic refresh not feasible
Route stays valid until:
Explicitly WITHDRAW or
TCP connection breaks
Periodic KEEPALIVE
Needed to check TCP connection
Just a single message
Independent of number of routes

## Slide 70: Network meltdown due to Run-away replication

## Slide 71: Packet replication loops
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast)
Forwarding loop
Network meltdown
+
=

## Slide 72: Packet replication loops
Packet replication Making multiple copies of a packet when you forward it (e.g. multicast)
Forwarding loop
No time to live (TTL) mechanism Packets can loop forever without ever being removed due to TTL expiry
Catastrophic network meltdown
+
+
=

## Slide 73: Ethernet address learning
11:11:11:11:11:11
22:22:22:22:22:22
33:33:33:33:33:33
Ethernet Address | Port
Switch layer 2 forwarding table
Port 1
Port 2
Port 3

## Slide 74: Ethernet address learning
11:11:11:11:11:11
22:22:22:22:22:22
33:33:33:33:33:33
Port 1
Port 3
Ethernet Address | Port
11:11:11:11:11:11 | 1
Switch layer 2 forwarding table
Unknown destination address: flood and learn source
Source Address | Destination Address | Payload
11:11:11:11:11:11 | 22:22:22:22:22:22 | …
Port 2

## Slide 75: Ethernet address learning
11:11:11:11:11:11
22:22:22:22:22:22
33:33:33:33:33:33
Port 1
Port 3
Ethernet Address | Port
11:11:11:11:11:11 22:22:22:22:22:22 | 1 2
Switch layer 2 forwarding table
Known destination address: unicast and learn source
Source Address | Destination Address | Payload
22:22:22:22:22:22 | 11:11:11:11:11:11 | …
Port 2

## Slide 76: Ethernet meltdown due to forwarding loop
Packet loop around the network at line rate
Number of packets grows exponentially

## Slide 77: Spanning Tree Protocol (STP)
STP removes loops by blocking links to form a spanning tree.
Wastes a lot of link capacity (no multipath)
Network melts down if STP doesn’t converge perfectly.

## Slide 78: Network meltdown due to Run-away state machine

## Slide 79: Typical 3-way adjacency finite state machine
State ONE-WAY
State TWO-WAY
State THREE-WAY
TX timer
TX HELLO(s=x)
TX timer
TX HELLO(s=x, n=y)
TX timer
TX HELLO(s=x, n=y)
RX HELLO(s=y)
-
RX HELLO(s=y, n=x)
-
RX HELLO(s=y, n=x)
-
RX HELLO(s=y, n=x)
-
X
Y
HELLO(s=x)
HELLO(s=x)
HELLO(s=x, n=y)
HELLO(s=x)
HELLO(s=y, n=x)
HELLO(s=y, n=x)
HELLO(s=y, n=x)
ONE-WAY
THREE-WAY
TWO-WAY
ONE
THREE-WAY
One HELLO message per timer interval (e.g. 10 seconds)
in each direction

## Slide 80: Run-away 3-way adjacency FSM
State NONE
State ONE-WAY
State TWO-WAY
TX timer
TX HELLO(s=x)
TX timer
TX HELLO(s=x, n=y)
TX timer
TX HELLO(s=x, n=y)
RX HELLO(s=y)
TX HELLO(s=x, n=y)
RX HELLO(s=y, n=x)
TX HELLO(s=x, n=y)
RX HELLO(s=y, n=x)
TX HELLO(s=x, n=y)
RX HELLO(s=y, n=x)
TX HELLO(s=x, n=y)
X
Y
HELLO(s=x)
HELLO(s=x, n=y)
HELLO(s=x, n=y)
HELLO(s=x, n=y)
HELLO(s=y, n=x)
HELLO(s=y, n=x)
HELLO(s=y, n=x)
NONE
THREE-WAY
ONE-
WAY
NONE
TWO-WAY
HELLO(s=y, n=x)
HELLO(s=x, n=y)
Non-stop line-rate of HELLOs
going back and forth

## Slide 81: Real life example: early draft of RIFT

## Slide 82: Network oscillation due to Run-away feedback loop

## Slide 83: Shortest path routing, bandwidth metrics
Congested router
High queueing delay, packet drops

## Slide 84: Desired situation: spread the load
This is what traffic engineering would do.

## Slide 85: Failed attempts at congestion-sensitive routing
Congestion => Advertise high delay metric
No congestion => Advertise low delay metric

## Slide 86: Failed attempts at congestion-sensitive routing
No congestion => Advertise low delay metric
Congestion => Advertise high delay metric

## Slide 87: Oscillation due to unstable feedback loop
Traffic volume
Time
Northern path
Southern path
Delay-based metrics have been attempted many times, and have failed as many times

## Slide 88: Take-aways for quantum control protocols
Make sure your protocols don’t have run-away scenarios
Beware of run-away replication
Beware of run-away state machines
Beware of run-away feedback loops

## Slide 89: Thank you.